## Slide 2: 6
Automotive Measurement and Math
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Use both customary and metric measuring systems.
Identify and use basic measuring tools.
Use decimal and metric conversion charts.
Use basic math skills.
Understand percentages and ratios.
Correctly answer ASE certification test questions that require a basic understanding of measurement and math.

## Slide 4: Measuring Systems
Two are commonly used in auto shop
  Customary or US customary
    Inches, pounds, etc.
  Metric (SI)
    Millimeters, grams, etc.

## Slide 5: Measuring Systems (Cont.)
Customary
  Originated with sizes taken from parts of human body
Metric (SI)
  Power of 10 for all basic units
Conversion chart
  Change measurement from one system to another
Decimal conversion chart
  Find equivalent values for fractions, decimals, and millimeters

## Slide 6: Conversion Chart

## Slide 7: Decimal Conversion Chart
(Parker Hannifin Corp.)

## Slide 8: Measuring Tools
Steel rule or scale
  Use to make low-precision linear measurements
  Customary rule
    Uses numbered lines to represent inches
    Uses unnumbered lines to represent fractions of inch
  Metric rule
    Uses unnumbered lines to represent millimeters
    Uses numbered lines to represent centimeters (10mm = 1cm)

## Slide 9: Measuring Tools (Cont.)
Pocket rule
  Typically 6″ long and fits in pocket
Combination square
  Sliding square mounted on steel rule
Tape measure
  Extends to several feet or meters in length
Yardstick or meterstick
  Use for large linear measurements up to one yard or one meter

## Slide 10: Calipers
Vernier caliper
  Use to make inside, outside, and depth measurements
(Starrett)

## Slide 11: Micrometers
Use to make very accurate measurements
  One ten-thousandth
  of inch
    0.0001″
    0.001 mm
Outside micrometer
  External dimensions
    Diameters
    Thicknesses
(Starrett)

## Slide 12: Micrometers (Cont.)
Inside micrometer
  Large holes
  Cylinders
  Part openings
Depth micrometer
  Use to measure depth of opening
(Starrett and Snap-on Tool Corp.)

## Slide 13: Reading a Micrometer
Note largest number visible on sleeve
Count sleeve graduation lines to the right
Note thimble graduation (round off)
Add all decimal values
  Add any full inches
Metric micrometers
  Read same way
(Starrett)

## Slide 14: Measuring Tool Rules
Never drop or overtighten micrometer or caliper
Store measuring tools where they cannot be damaged
Grasp micrometer frame in palm and turn thimble with thumb and finger
Hold micrometer squarely with work

## Slide 15: Measuring Tool Rules (Cont.)
Rock or swivel micrometer as it is touched on round parts
Place thin film of oil on micrometer and caliper surfaces during storage
Always check for accuracy using standardized gauge block after dropping or prolonged use

## Slide 16: Feeler Gauges
Use to measure small clearances or gaps between parts
Flat feeler gauge
  Precision-ground steel blades, various thicknesses
    Size written on each blade in thousandths of an inch or hundredths of a millimeter
Wire feeler gauge
  Precise-sized wires labeled by diameter of thickness
  Use to measure slightly larger gaps and spaces

## Slide 17: Dial Indicator
Measures part movement in thousandths of an inch
  Hundredths of a millimeter
  Use to check
    Gear teeth backlash (clearance)
    Shaft end play
    Cam lobe lift

## Slide 18: Using a Dial Indicator
Mount indicator securely
  Position dial plunger
Partially compress indicator plunger
  Lock in place
Move or rotate part
  Read indicator
  Subtract lowest reading from highest
(Central Tool Co.)

## Slide 19: Angle Measurement
Circle divided into 360 equal parts called degrees
  Abbreviated using “deg.” or (°)
One-quarter of circle equals 90°

## Slide 20: Temperature Measurement
Measure using temperature gauges or thermometers
Available in either Fahrenheit (F°) or metric Celsius (C°)

## Slide 21: Torque Wrenches
Use to apply specific amount of turning force to fastener
Read
  Foot pounds (ft-lb)
  Newton-meters (N  m)

## Slide 22: Other Measurements and Measuring Tools
Pressure gauge
  Use to measure air or fluid pressure
    Pounds per square inch (psi)
    Kilograms per square centimeter (kg/ cm²)
    Kilopascals (kPa)
Vacuum gauge
  Use to measure negative pressure or vacuum
    Inches of mercury (in/ Hg)
    Metric kilograms per square centimeter (kg/ cm²)

## Slide 23: Other Measurements and Measuring Tools (Cont.)
Telescoping gauge
  Measures internal part bores or openings
Hole gauge
  Measures very small holes in parts

## Slide 24: Review of Shop Math
Auto technicians work with whole numbers, fractions, and decimals every day
  Calculate
    Measurements
    Clearances
    Part prices
    Labor charges
    Tax percentages
    Total charges

## Slide 25: Addition
Combining two or more numbers to find total quantity
  Result called sum
Write large numbers, or long series of numbers, in column
Use for adding up costs of parts and labor

## Slide 26: Subtraction
Taking away certain quantity from another
  Amount left after subtracting called remainder
Use to determine customers’ bills after deposit
Useful for checking paychecks for tax deductions

## Slide 27: Division
Finds out how many times a number is contained in another number
  Number being divided is dividend
  Number that dividend is divided by is divisor
  Answer is quotient
Use to determine unit costs
  If 10 fuel pumps cost $100.00, then 1 fuel pump costs?

## Slide 28: Multiplication
Shortcut for adding same number over and over
  Number by which another number is multiplied is multiplier
  Result of multiplication is product

## Slide 29: Fractions
Represent portion of whole number
  Written as two numbers, one over the other or one beside the number
  Number below line or slash called denominator
    How many parts the whole is divided into
  Number above line or slash called numerator
    How many parts are present in the fraction

## Slide 30: Decimal Fractions
Also have numerator and denominator
  Denominator always a multiple of 10 that is never written
    Use decimal point, a dot or period, instead
    For example, 9/10 is written 0.9
  Number of digits to right of decimal point tells what multiple of 10
    Tenths, hundredths, thousandths, etc.

## Slide 31: Decimal Fractions (Cont.)
Zero placed
  Between number and decimal point changes value of number (.45 is not the same as .045)
  To right of decimal number does not change value of number (.45 is the same as .450)
  To left of decimal point does not change value of number (0.45 is the same as .45)

## Slide 32: Addition and Subtraction of Decimals
Line up decimal points in column
Decimal point in answer must be in same position as decimal point in column

## Slide 33: Multiplication of Decimals
Decimal points do not need to be aligned
Multiply numbers ignoring decimal points
Count total number of decimal points to right of both numbers
  Starting from right digit, count to left the same number of digits in answer
  Place decimal point to left of last digit counted

## Slide 34: Division of Decimals
When neither dividend nor divisor contain decimal points, but division does not come out even
  Place decimal point to right of last number of dividend
  Add one or more zeros after decimal and continue dividing to number of spaces necessary

## Slide 35: Division of Decimals (Cont.)
When dividend has decimal and divisor does not
  Divide as usual
  Place decimal point in answer directly above decimal point in dividend

## Slide 36: Division of Decimals (Cont.)
When divisor has decimal point
  If dividend does not have decimal point, add one to far right
  If dividend has decimal point, move it one place to the right for each decimal place in divisor
    Use zeros as placeholders if needed
  Divide as usual
  Place decimal point in answer directly above relocated decimal point in dividend

## Slide 37: Percentages
Quantities expressed as part of 100
10% equal to 10 out of every 100
Commonly used to calculate tax on parts
To find percentage of any number
Convert percentage to decimal
Drop percentage sign and move decimal left two places
Multiply decimal by number

## Slide 38: Ratios
Mathematic expression comparing two numbers
Represent how many of one number there is compared to another
Ratio of 2 to 1 can be written 2:1 or 2/1
Ratios are commonly used when expressing relationships between gears
If two gears have 3:1 gear ratio, one gear would turn three revolutions to only one revolution of other gear