## Slide 2: 8
Fasteners, Gaskets, Seals, and Sealants
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Identify commonly used automotive fasteners.
Select and use fasteners properly.
Remove, select, and install gaskets, seals, and sealants correctly.
Summarize safety rules relating to fasteners, gaskets, seals, and sealants.
Correctly answer ASE certification test questions that require a knowledge of fasteners, gaskets, seals, and sealants.

## Slide 4: Fasteners
(Deere & Co.)

## Slide 5: Bolts and Nuts
Bolt size
  Outside diameter of bolt threads
Bolt head size
  Distance across outer sides of bolt head
Bolt length
Measured from bottom of bolt head to threaded end of bolt
Thread pitch or thread coarseness
  Number of threads per inch

## Slide 6: Bolts and Nuts (Cont.)
(Ford)

## Slide 7: Bolts and Nuts (Cont.)
Thread types
  Coarse (UNC)
  Fine (UNF)
  Metric (SI)
Bolt grade
  Indicates bolt’s tensile strength
Bolt description
  Series of numbers and letters describing bolt

## Slide 8: Bolt Description Numbers

## Slide 9: Nut Types
(Deere & Co.)

## Slide 10: Washers
Use under bolt heads and nuts
  Flat washer
    Increases clamping surface under washer
  Lock washer
    Prevents bolt or nut from coming loose under stress or vibration
  Lock tabs or lock plates
    Perform function of both flat washers and lock washers

## Slide 11: Screw Types
Machine screws
  Similar to bolts but normally have screw-type heads
Sheet metal screws or tapping screws
  Used on plastic and sheet metal
  Wide range of head configurations and sizes
(Deere & Co.)

## Slide 12: Snap Rings
Fit into groove in part
Commonly hold shafts, bearings, gears, pins, and components in place
Require snap ring pliers to remove and install

## Slide 13: Keys and Set Screws
Keys
  Fit into keyseat or slot cut into shaft and keyway cut into mating part
Set screws
  Lock part onto shaft
  Used with or without key
  Hex (Allen) or screwdriver

## Slide 14: Keys and Screw Sets (Cont.)
(Florida Dept. of Voc. Ed.)

## Slide 15: Splines
Series of slots cut into shaft and mating part
  Allow gears or collars to slide but not rotate
    Manual transmissions
    Clutches
    Drive shaft yokes

## Slide 16: Adhesives
Special glues widely used in vehicles
  Body moldings
  Rubber weather stripping
  Body emblems
Some stay soft and pliable while others dry hard
Some take hours to dry while others dry in seconds

## Slide 17: Torquing Bolts and Nuts
Torque specifications
  Tightening specifications given by manufacturer
Torque-to-yield
  Tightening method where bolt is tightened to specific torque and then additional number of degrees

## Slide 18: Torquing Bolts and Nuts (Cont.)

## Slide 19: Bolt Tightening Sequence
Also called torque pattern
  Used to make sure parts are fastened evenly
  Uses crisscross pattern
Uneven tightening
  Breaks
  Leaks
  Warping

## Slide 20: Using a Torque Wrench
Pull steadily on wrench
Clean fastener threads
Avoid using swivel joints
Look straight down at scale
Only use torque value chart when no manufacturer's specifications are available
If torque pattern is not available, use general crisscross pattern

## Slide 21: Using a Torque Wrench (Cont.)
Pull only on handle of torque wrench
  Do not allow beam of beam-type wrench to touch anything
Tighten bolts in four steps
Retorque when required

## Slide 22: Thread Repairs
Minor
  Cleaned up with thread chaser
Major
  Must be repaired with either a tap or a die
    Tap is threaded tool for cutting internal threads
    Die cuts external threads

## Slide 23: Tap and Die Rules
Never force tap handle
Keep tap and die well oiled
Always use right size tap in correct size hole
Use coarse threads when tapping soft metal

## Slide 24: Thread Repairs (Cont.)
Tapping oversize
  When thread chaser or tap cannot be used to clean up damaged threads, hole can be tapped and threaded oversize
  Use drill and tap size chart

## Slide 25: Thread Repairs (Cont.)

## Slide 26: Thread Repairs (Cont.)
Thread repair insert
  Use when oversize hole and fastener is not acceptable
  Insert replaces damaged internal threads
  Allows use of original size bolt
(Chrysler and The Eastwood Company)

## Slide 27: Removing Damaged Fasteners
Locking pliers
  Remove broken bolts, screws, and fasteners
Stud puller
  Removes studs and bolts broken off above surface of part
If fastener is too short to grasp
  Cut slot with hacksaw
  Weld on new head

## Slide 28: Removing Damaged Fasteners (Cont.)
If fastener is broken flush
  Use hammer and punch
Screw extractor or “easy out”
  Removes bolts broken flush or below surface
Try drilling hole almost as large as bolt, then use tap or punch to remove excess
Rust penetrant dissolves rust or corrosion
  Use to aid removal

## Slide 29: Removing Damaged Fasteners (Cont.)

## Slide 30: Gaskets and Seals
Gasket
Soft, flexible material placed between parts to prevent leakage
  Fiber
  Rubber
  Neoprene
  Cork
  Treated paper
  Thin steel
(Fiat)

## Slide 31: Using Gaskets
Inspect for leaks prior to disassembly
Clean off old gaskets carefully
  Use scraper or wire brush
  Be extra careful with aluminum and brass
Wash and dry parts thoroughly using solvents
  Dry with compressed air
Compare new gasket to shape of mating surface
  Must match perfectly

## Slide 32: Using Gaskets (Cont.)
Use sealer if needed
Screw in all bolts by hand
Use crisscross pattern and tighten in steps
  Torque one step at a time if required

## Slide 33: Sealers
Coat gasket to prevent leakage
Hold gaskets in place during assembly
Hardening sealers
  Use on permanent assemblies
  Fills uneven surfaces
  Resistant to heat and chemicals
Shellac
  Sticky, nonhardening sealer
  Use on fiber gaskets

## Slide 34: Sealers (Cont.)
Form-in-place gaskets
  Special sealers used in place of fiber or rubber gaskets
    Room temperature vulcanizing (RTV)
    Anaerobic sealer

## Slide 35: Sealers (Cont.)
(Fel-Pro Gaskets)

## Slide 36: Seals
Prevent leakage between stationary part and moving part
  Found in almost any part containing fluid and moving parts
  Allow shafts to spin or slide without fluid leakage
  Normally made of synthetic rubber molded onto metal bodies

## Slide 37: Seal Rules
Inspect for leakage prior to disassembly
  Look for bent shafts, misaligned housing, or damaged parts
Remove old seal carefully
  May require special puller
Inspect shaft for wear or burrs
  File off burrs
  Polish, repair, or replace worn shafts

## Slide 38: Seal Rules (Cont.)
Compare old seal to new one
  Both inside and outside diameter should match
  Slip seal over shaft and verify snugness
Install new seal
  Coat outside of seal housing with sealer
  Coat inner lip with system fluid
  Backward installation will cause heavy leakage
  Verify it is squarely and firmly seated

## Slide 39: O-Ring Seals
Stationary seal that fits into groove between two parts
Form leakproof joints by applying pressure to multiple surfaces
Coat with system fluid before installation

## Slide 40: Other Information
Special gaskets and seals
  Installation techniques
These special situations are discussed in later chapters of this textbook