## Slide 2: 18
Circuit Types and Ohm’s Law
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Compare the operating characteristics of series, parallel, and series-parallel circuits.
Explain the operation of a frame-ground circuit.
Recall the three Ohm’s law formulas that express the relationships among voltage, current, and resistance.

## Slide 4: Objectives
Explain how changes in voltage and resistance affect current.
Use Ohm’s law and circuit-type formulas to calculate unknown circuit values.
Use the formula for calculating electric power or wattage.
Interpret electrical prefixes.

## Slide 5: Circuit Types
Circuit
  Closed electrical path for current
Three main types of circuits
  Series
  Parallel
  Series-parallel circuits
Automotive systems also use frame-ground circuits

## Slide 6: Series Circuit
Only one path for current
One or more loads wired into this single path
If one bulb burns out, all other lights go out

## Slide 7: Parallel Circuit
Has more than one path for current
Two or more loads placed on separate paths
One burned-out light does not affect other bulbs

## Slide 8: Series-Parallel Circuit
Combination of series circuit and parallel circuit
Some components wired in series, others wired in parallel

## Slide 9: Frame-Ground Circuit
Also called one-wire circuit
Uses vehicle’s metal structure to return electricity to power source
Eliminates need to run wires back from components

## Slide 10: Ohm’s Law
Formula set expressing relationships between voltage, current, and resistance in electric circuit
Ohm’s law stated as three different formulas
If any two of three electrical values in circuit are known, third value can be calculated

## Slide 11: Ohm’s Law (Cont.)
E = I × R
  Voltage equals current multiplied by resistance
    Volts = amps × ohms
I = E ÷ R
  Current equals voltage divided by resistance
    Amps = volts ÷ ohms
R = E ÷ I
  Resistance equals voltage divided by current
    Ohms = volts ÷ amps

## Slide 12: Ohm’s Law (Cont.)

## Slide 13: Ohm’s Law (Cont.)
1 volt needed to push 1 amp of current through 1 ohm of resistance
If any one value changes, it affects others

## Slide 14: Change in Resistance
Alters amount of current in circuit
  If resistance is low, current will be high
  If resistance is high, current will be low
Most electrical problems caused by changes in circuit resistance

## Slide 15: Change in Voltage
Affects amount of current in circuit
  Rise in voltage increases current
  Drop in voltage decreases current

## Slide 16: Change in Current
Result of increased or decreased voltage or resistance
  Without sufficient current, load will not function properly

## Slide 17: Series Circuit Calculations
Three rules apply to series circuits
Current is same everywhere
Total resistance (Rt) is sum of all resistances
Voltage drop across each resistance equals voltage applied
  Voltage used by all resistance elements equals total voltage

## Slide 18: Series Circuit Calculations (Cont.)

## Slide 19: Parallel Circuit Calculations
Parallel circuits also have three rules
Total current (It) is sum of all branch currents
Total circuit resistance is less than resistance in any one branch
Total voltage equals supply voltage, and voltage is the same throughout circuit

## Slide 20: Parallel Circuit Calculations (Cont.)

## Slide 21: Series-Parallel Circuit Calculations
Equivalent resistance
  Total resistance found by calculating resistance of each parallel section and then adding series resistances

## Slide 22: Series-Parallel Circuit Calculations (Cont.)

## Slide 23: Complex Series-Parallel Circuits
When working with complex series-parallel circuits
  Start by working with parallel sections
  Arrive at R for each section
  Add any series resistance to find total resistance

## Slide 24: Complex Series-Parallel Circuits (Cont.)

## Slide 25: Electric Power Calculations
Electric power
  Work done by electric current
  Unit of measurement is watt
Calculate circuit’s electric power with its current and either voltage or resistance
  P (in watts) = E × I or P = I2 × R

## Slide 26: Prefixes for Electrical Units
Electrical values may be very large or very small
  Prefixes indicate multiplier or exponent
Examples include
  MΩ (megohms) = 5,000,000 Ω
  10 kΩ (kilohms) = 10,000 Ω
  32 mA (milliamperes) = 0.032 A
  12 μF (microfarads) = 0.000 012 farad

## Slide 27: Prefixes for Electrical Units (Cont.)