## Slide 2: 19
Electric and Electronic Components
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Identify electric components.
Explain the function and operation of electric and electronic components.
Interpret electric and electronic component ratings and values.

## Slide 4: Objectives
Recognize the symbols and letter designations for electric and electronic components.
Recall the properties of semiconductor materials.
Recall the common types of transistors.
Give examples of photonic devices.

## Slide 5: Electric Components

## Slide 6: Resistors
Limits and controls current flow in circuit
Various shapes and sizes, depending on function
Fixed resistors have set ohms value that does not change

## Slide 7: Variable Resistors
Has adjustable range of internal resistance
Two types of variable resistors
  Rheostats
  Potentiometers

## Slide 8: Rheostats
One terminal wires to one end of resistance unit
Other terminal connects to sliding contact
Turning control knob moves contact and alters resistance

## Slide 9: Potentiometer
Variable resistor with three electrical connections
One at each end of resistance unit
One for sliding contact

## Slide 10: Switches
Connects or disconnects power supply in circuit
Push-button
  Spring-loaded button that makes or breaks electrical connection
Push-pull
  Stays in each position until moved

## Slide 11: Switches (Cont.)
Thermal
  Opens and closes with changes in temperature
Pressure
  Reacts to changes in internal pressure
Mercury
  Uses liquid mercury to open and close its switch contacts
Dozens of switches found in modern vehicles

## Slide 12: Switches (Cont.)

## Slide 13: Capacitors
Storage device for electrons or electrical energy
How capacitors work
  When dc applies to capacitor, electrons build up on conductor strip
  Capacitor becomes charged
  When charge equals dc voltage, electrons can no longer flow

## Slide 14: Capacitors (Cont.)
Small capacitors
  Can be used to stop dc voltage
Larger capacitors
  Can be used to even out voltage fluctuations
Alternating current
  Can pass through capacitor
  Charges while current is in one direction
  Discharges back into circuit when current changes direction

## Slide 15: Capacitors (Cont.)
In vehicles
  Used as noise suppressor
  Found in computer circuits, sound systems, navigation systems, and printed circuits
Capacitor’s size or storage ability rated in farads (F)
  Most small capacitors rated in microfarads (μF) or picofarads (pF)

## Slide 16: Fuses
Protects circuit from damage caused by excess current
Short circuit
  Results when hot wire touches any ground
Fuse ratings
  Amount of current fuse can handle before its element melts

## Slide 17: Fuse Panels
Plastic housing with metal terminals
Holds fuses and other electric components
Most mount under vehicle’s dash

## Slide 18: Fuse Links
Section of smaller gauge wire connected in series with larger gauge circuit wiring
Designed to serve as very large fuse
Usually wired between12-volt battery and fuse panel

## Slide 19: Circuit Breakers
Protects circuit from damage from excess current
Not ruined when activated or “tripped”

## Slide 20: Self-Resetting Circuit Breaker
Can sense high-current conditions and disconnect circuit
Automatically reconnects circuit after it cools

## Slide 21: Coils
Also called choke or inductor
  Insulated wire loops placed close together to create electromagnetic field
    Wrapped around iron core to strengthen electromagnetic properties
  Used in electrical circuits to resist current and voltage fluctuation
    Transformers, solenoids, motors, relays, and other components

## Slide 22: Transformers
Uses two sets of coils to change levels of voltage and current
Impedance
  Resistance to alternating current at given frequency
Turns ratio
  Represents relationship between number of wire windings, wraps, in each coil

## Slide 23: Transformers (Cont.)
Isolation
  Has turns ratio of one to one (1:1)
  Induced voltage in second coil is the same as first coil’s voltage
  Isolates one circuit from another

## Slide 24: Transformers (Cont.)
Step-up
  Second coil has more windings than first coil
  If turns ratio is 1:2, application of 12 volts to first coil produces 24 volts in second coil

## Slide 25: Transformers (Cont.)
Step-down
  Second coil has fewer windings than first coil
    Reduces output voltage compared to input voltage
  If turns ratio is 2:1, 12 volts in first coil produces output of only 6 volts in second coil

## Slide 26: Transformers (Cont.)
Voltage and current in transformer are inversely proportional
  When transformer increases voltage, current decreases
  If transformer reduces voltage, current increases
    Current sacrificed to gain voltage
    Voltage sacrificed to gain current

## Slide 27: Relays
Use small input current to control larger current in circuit
Allows wires to be much smaller than otherwise needed

## Slide 28: Solenoids
Electromagnets that move metal core, or plunger
When current breaks, spring action pushes core back out
  Uses
    Close large electrical contacts
    Move parts into engagement

## Slide 29: Electric Motors
Use magnetic fields to produce powerful rotating action
Parts of motor
  Armature
  Commutators
  Brushes
  Magnets

## Slide 30: Electric Motors (Cont.)

## Slide 31: Electronic Components
Also called solid state components
  Composed of semiconductor material
  Allows device to control electricity
    Less energy consumption

## Slide 32: Semiconductors
Crystal material that can conduct or insulate
P-type semiconductor
  Doped so that it has excess protons
  P stands for positive
N-type semiconductor
  Doped so that it has excess electrons
  N stands for negative

## Slide 33: Diodes
Made by joining N-type semiconductor with P-type semiconductor
Blocks direct current in one direction and passes it in other
PN junction
  Common edge of P-type and N-type semiconductors

## Slide 34: Diodes (Cont.)
Forward bias
  Connected so that it acts as conductor
Reverse bias
  Connected so that it acts as insulator
Depletion area
  Area surrounding PN junction

## Slide 35: Diodes (Cont.)

## Slide 36: Diodes (Cont.)
Reverse bias voltage
  Rating of maximum voltage diode can block without damage
Rectification
  Conversion of alternating current to direct current

## Slide 37: Half-Wave Rectification
Produced by single diode in series with ac source
Only half of each ac wave allowed through

## Slide 38: Full-Wave Rectification
Allows both halves of each ac wave through
Both halves flow in the same direction
Diodes commonly used inside charging system alternators

## Slide 39: Zener Diodes
Serves as voltage regulator
Conducts current when forward biased
Blocks current when reverse biased
When specific reverse-bias voltage is reached, it conducts current

## Slide 40: Transistors
Semiconductor that regulates current or voltage
Transfers or changes with electric stimulation
Can act as switch for electronic signals or current amplifier
Bipolar junction transistor (BJT)
  Made by joining three semiconductor materials

## Slide 41: Transistors (Cont.)
NPN transistor
  Two N-type semiconductors and one P-type semiconductor bonded together
PNP transistor
  Two P-type semiconductors and one N-type semiconductor bonded together

## Slide 42: Transistors (Cont.)
Transistor and relay can perform same function
Transistor vs. relay
  Smaller
  No moving parts

## Slide 43: Transistors (Cont.)
(Echlin)

## Slide 44: Piezoelectric Crystal
Produces low current output when physical pressure is applied
Makes a microphone when linked to diaphragm

## Slide 45: Photonic Devices
Any device that can emit or detect light
Photon
  Particle of electromagnetic light energy
Photonics is a fast-growing field of electronics
  Photonic semiconductors are now being found in automotive electronics

## Slide 46: Light Emitting Diodes
LED
Semiconductor that emits light when electrically energized
More efficient than other light sources

## Slide 47: Fiber Optics
Field of electronics which uses light to carry data through small strands of plastic or glass fiber

## Slide 48: Photovoltaic Cells, Photoresistors, and Photodiodes
Photovoltaic or solar cell
  Converts light directly into current
Photoresistor
  Acts as resistor in dark but changes to conductor in light
Photodiode
  Can produce low voltage when excited by light
  Control current by allowing current flow

## Slide 49: Liquid Crystal Displays
Liquid crystal display (LCD)
  Fluid crystal material sealed between two glass plates
  Polarizes light to display numbers, letters, or other images