## Slide 2: 20
Electrical Tools and Test Equipment
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Identify tools that are commonly used during electrical repairs.
Summarize the use of test equipment for various vehicle systems.
Summarize the use of multi-system test equipment such as scan tools and engine analyzers.
Select the proper tool or tester for the job.

## Slide 4: Soldering Tools
Solder
  Alloy with relatively low melting point compared to other metals
Soldering
  Process of using heat and molten solder to join wires, terminals, and other components
  Best method for making electrical connections
  Low resistance, resist corrosion, and vibration failure

## Slide 5: Soldering Tools (Cont.)
Soldering torch (A)
  Burns butane gas to instantly generate heat
Soldering iron (B)
  Tip is smaller and better suited to delicate work on circuit boards
Soldering gun (C)
  High power rating and trigger-operated

## Slide 6: Soldering Tools (Cont.)
Flux brush
  Used to apply paste-type flux to joint
Flux
  Chemically cleans metal surfaces
    Molten solder bonds with base metals properly
Soldering picks
  Used to scrape corrosion from components before applying solder

## Slide 7: Soldering Tools (Cont.)
Heat sink
  Spring-loaded, clamp-on aluminum device
  Helps prevent overheating of electronic components
Desoldering bulb
  Tool for removing molten solder during repairs

## Slide 8: Soldering Tools (Cont.)
Soldering sponge
  Soaked in water and used to clean tip of soldering gun or iron
Holding devices
  Free technician’s hands to use soldering gun and solder

## Slide 9: Wire Stripping Tools

## Slide 10: Crimp Connecting Tools
Crimp connectors
  Easy way of joining wires or installing terminal
Crimping pliers
  Crushes metal part of connector around wire conductor

## Slide 11: Scan Tools
Check operation
Vehicle sensors
Actuators
Wiring
Computer
(Snap-on Tool Corp)

## Slide 12: Test Lights
Check circuits for power or continuity (complete circuit path)
  Energized by circuit voltage
Noid lights
  Check for power in wiring harness going to electronic fuel injectors

## Slide 13: Multimeters
Also called volt-ohm meter or VOM
  Measures exact electrical values in vehicle circuits
  Combines voltmeter, ohmmeter, and ammeter into one unit
Analog multimeter
  Needle or pointer shows electrical readings
Digital multimeter
  Liquid crystal display shows digital readout

## Slide 14: Multimeters (Cont.)

## Slide 15: Multimeters (Cont.)
Digital-analog meter
  Digital meter with alphanumeric display and bar graph to show fluctuating electrical values
Inductive pickup
  Does not have to touch metal components in circuit

## Slide 16: Inductive Wire Tracers
Finds internal breaks in wires and disconnected wires or terminals
  Pulse generator connects to circuit
  Inductive probe moves along wire
  Tracer makes audible beeping sound if wire has continuity and carries pulsing signal

## Slide 17: Oscilloscopes
Also called scope
  Displays line pattern, or trace
  Represents circuit voltages in relation to time
  Handheld version has oscilloscope and multimeter
(OTC/SPX Corp.)

## Slide 18: Load Testers
Tests condition
12-volt batteries
Charging systems
Starting systems

## Slide 19: Charging System Analyzers
Quickly measures charging system voltage to determine alternator operation

## Slide 20: System-Specific Test Equipment
Keyless entry tester
  Checks condition of key chain sending unit and signal sensor of keyless entry system
Park assist tester
  Troubleshoots output from laser at rear of vehicle in park assist system
  Tire pressure monitor calibration tool
  Used to calibrate and test tire pressure sensors

## Slide 21: Diesel Test Equipment
Glow plug analyzer
  Tests diesel glow plugs and engine’s operating condition