## Slide 2: 27
Hybrid Drive Systems Diagnosis and Repair
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Use on-board diagnostics to find the source of problems in a hybrid drive system.
Recall the safety measures that must be followed when working on high-voltage, high-current hybrid drive systems.
Perform basic tests to verify hybrid drive trouble codes.

## Slide 4: Objectives
Carry out proper procedures for safely removing and replacing a battery pack, an HV power control module, HV power cables, control modules, and motor-generator assembly.
Correctly answer ASE certification test questions about hybrid drive systems diagnosis and repair.

## Slide 5: Hybrid Problem Diagnosis
Extensive on-board diagnostic systems
Locate source of system problems
Monitor hundreds of operating conditions
Turn on warning lights

## Slide 6: Hybrid Problem Diagnosis (Cont.)
Hybrid ground fault interrupter
  Constantly monitors system for high-voltage leakage into chassis
Glowing malfunction indicator light means use a scan tool to retrieve stored trouble codes

## Slide 7: Hybrid Service Safety
Remove your jewelry
Wear eye protection
Wear insulating gloves
Wear rubber-soled shoes
Keep a fire extinguisher nearby
Follow towing safety procedures
Disable the hybrid drive when working
Set up a high-voltage buffer zone
Remove the high-voltage disconnect

## Slide 8: HV Battery Service
Hybrid battery packs have a warranty from manufacturer
Some offer full HV battery replacement for up to 8 years or 100,000 miles
HV batteries very dependable and seldom fail
  Can lose efficiency after extended service

## Slide 9: Diagnosing HV Battery Problems
Hybrid control module will check
  Circuit conditions when HV battery is discharging
  While powering electric drive motor(s)
  While being recharged by motor-generator
Trouble codes stored in control module if any electrical value is not within specifications

## Slide 10: Diagnosing HV Battery Problems (Cont.)
Hybrid dash displays that show
  HV battery charge
  Temperature and condition
Display will warn driver if diagnostic system detects problems with
  HV battery
  HV power cables
  HV power control module
  Other components

## Slide 11: Diagnosing HV Battery Problems (Cont.)
Scan tool will also quickly identify problems with
  HV battery
  Motor-generator
  High-voltage electrical connections
  Hybrid control module
  HV power control module
Scan tool can also be used to compare actual operating voltages to those on dash display

## Slide 12: Diagnosing HV Battery Problems (Cont.)
If HV battery fails to accept and hold charge, trouble code will be set
Hybrid control module will trigger malfunction indicator light in dash display
Replace failed HV batteries with new or reconditioned units

## Slide 13: Checking HV Battery Relays and Contactors
Very large relays with contact points
  Turn such high electrical load on and off, lugs become burned and pitted
  If burned enough, lugs develop high resistance
  Not able to carry enough current to HV PCM and motor-generator

## Slide 14: Checking HV Battery Relays and Contactors (Cont.)
Pinpoint test on high-voltage contactor
Remove or disconnect HV battery
Measure resistance across closed contactors with key on
Then with key off
If measurements not within specifications, replace contactors

## Slide 15: HV Power Cable Service
Note conductor resistance values on scan tool
If not within specifications
  Tighten or repair cable ends
  Replace HV power cables, if needed

## Slide 16: HV Power Cable Service (Cont.)
If scan tool shows ground fault problem
  Place test lead on one end of cable terminal
  Place other to frame or body ground
  If reading lower than specifications, insulation may be leaking high voltage to ground
(Toyota)

## Slide 17: HV Power Cable Service (Cont.)
To replace HV power cable
Disconnect both ends of cable
Remove clips securing power cable to vehicle
Install new power cable in reverse order

## Slide 18: HV Power Control Module Service
Faulty HV PCM trip various trouble codes, indicating which circuit might be faulty
Some hybrid vehicles use separate converter, rectifier, and three-phase circuits
  If scan tool indicates specific circuit board problem, consider replacing just failed circuit board

## Slide 19: HV Power Control Module Service (Cont.)
Bad high-power contactor lugs in HV PCM
  Burn and develop high resistance after prolonged service
Bad contactor lugs
  Prevent normal current flow through HV PCM and to motor-generator
Some hybrid vehicles use discrete inverters
  Remove and replace defective inverter
Sometimes circuit board in HV PCM can fail and require replacement

## Slide 20: HV Power Control Module Replacement
Use high-voltage safety gear and tools
Disable HV battery
Disconnect low-voltage connections and wiring harness from HV PCM
Drain HV cooling system
Remove coolant lines from side of HV PCM

## Slide 21: HV Power Control Module Replacement (Cont.)
Disconnect five or more high-power cables from the HV PCM
  Wrap electrical tape around each exposed HV battery cable end
Remove hold-down machine screws connecting HV PCM to body
Reinstall in reverse order
Erase stored trouble codes
  Rescan hybrid drive system

## Slide 22: Hybrid Cooling System Service
If cooling system fails, components overheat
If air cooled, listen for normal operation of cooling fan
If water cooled, place stethoscope on electric pump to determine if running when under high electrical load

## Slide 23: Hybrid Cooling System Service (Cont.)
If you find inoperative cooling fan blower motor, replace it like a climate control blower
With liquid system, disconnect hoses and wires going to pump motor before replacement

## Slide 24: Motor-Generator Service
Normally, motor-generator is trouble free
If car is hit by lightning or used for extended period
  Motor-generator can fail
  Stator coil windings in unit can short or burn open

## Slide 25: Motor-Generator Service (Cont.)
Motor-generator trouble code can indicate various problems
Short coils
Poor power cable connections
Permanent magnet armature damage
Motor speed sensor failure
Other things

## Slide 26: ECM’s That Can Affect Motor-Generator Operation
(Toyota)

## Slide 27: Testing a Motor-Generator
To perform motor-generator resistance test
Wear insulated gloves and safety glasses, and use insulated tools
Disable or disconnect HV battery
Disconnect three power cables connected to motor-generator
Inspect both sets of orange cable conductor terminals for damage from overheating and burning

## Slide 28: Testing a Motor-Generator (Cont.)
Connect ohmmeter to each conductor going to motor-generator stator windings and to ground
Record and compare ohmmeter reading for each of three legs
Normally, each leg of stator windings should have same reading

## Slide 29: Testing a Motor-Generator (Cont.)
Using stethoscope
Raise vehicle
Drive in all-electric mode until system attempts to start engine
Listen during electric propulsion and engine starting
Place stethoscope against traction motor’s side
  Listen for mechanical noises that indicate failure

## Slide 30: Removing and Installing a Motor-Generator
Disable electric drive system and HV battery
Remove CV axles or drive shaft, wires, fluid lines, linkages, and body to-transmission mounting fasteners
Remove transaxle or transmission
Disconnect any cooling lines, wires, and flex or end plates from motor generator housing

## Slide 31: Removing and Installing a Motor-Generator (Cont.)
Install plastic ring tool between armature and stator
Remove armature bolts and pull armature off crankshaft flange with wheel puller
Unbolt and remove stator housing from engine block

## Slide 32: Removing and Installing a Motor-Generator (Cont.)
Check resistance and condition of armature sensor
Install new motor-generator in reverse order
Bolt and torque armature to crankshaft
Install plastic spacer ring tool over armature
Torque stator housing bolts to specs

## Slide 33: Typical Engine-Mounted Motor-Generator
(Porsche)

## Slide 34: Hybrid Wiring Problems
Certain electrical/electronic circuit issues are difficult to diagnose and repair
  Poor electrical connections
  Broken wire conductors
  Shorted wires

## Slide 35: Hybrid Wiring Problems (Cont.)
If scan tool shows issue with component that tests good, check for wiring problems in corresponding circuit
Use factory diagrams to locate items possibly affecting operation of that circuit

## Slide 36: Factory Diagram