## Slide 2: 32
Charging System Technology
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Describe the construction of major 12-volt charging system components.
Explain charging system indicators and instrumentation.
Explain the construction and operation of hybrid charging systems.

## Slide 4: Objectives
Compare the operation of a 12-volt charging system to that of a hybrid charging system.
Correctly answer ASE certification test questions that require a knowledge of charging system fundamentals.

## Slide 5: 12-Volt Charging System Functions
Recharges battery after engine cranking or after electrical accessory use with engine shut off
Supplies all12-volt electricity when engine is running
Provides 13-15 volt output, slightly higher than fully-charged battery at 12.6 volts

## Slide 6: 12-Volt Charging System Functions (Cont.)
Changes current and voltage output to meet different electrical loads
Provides smooth dc for proper function of all vehicle’s electronic circuits

## Slide 7: Basic Charging Circuit

## Slide 8: 12-Volt Charging System Parts
Alternator (ac generator)
Voltage regulator
Drive belt
Charge indicator
Charging system harness
Battery
ECM

## Slide 9: 12-Volt Charging System
During engine cranking, battery supplies all electricity for use
When engine starts running, charging system takes over
Voltage regulator keeps alternator output at preset charging voltage (13–15 volts)
  Since this is higher than battery voltage (12.6 volts), current flows back into battery

## Slide 10: Alternator
Simplified alternator has two main parts
  Rotor
    Located in alternator housing center
    Creates rotating magnetic field
  Stator
    Stationary set of windings surrounds rotor
    Output winding in alternator

## Slide 11: Alternator (Cont.)
Produces alternating current (ac) output
Automobile electrical systems designed to use direct current (dc)
  Cannot use ac as it comes out of alternator’s stator
Alternator current must be rectified before entering electrical system
  Changed into direct current

## Slide 12: Alternator Components
Rotor
Brush assembly
Rectifier
Stator
Alternator housing
Fan and pulley
Voltage regulator

## Slide 13: Alternator Components (Cont.)
(Ford)

## Slide 14: Alternator Components (Cont.)
Alternator rotor assembly
  Consists of field windings mounted on shaft
Alternator bearings
  Used to produce low-friction surface for rotor shaft
  Needle or ball types

## Slide 15: Alternator Components (Cont.)
Alternator slip rings
  Mounted on rotor shaft to provide dc current to field windings
  Each end of field windings connects to a slip ring
Alternator brushes
  Ride on slip rings to make sliding electrical connection
Brush springs
  Hold brushes in contact with slip rings

## Slide 16: Alternator Rectifier
Or diode assembly
Uses six diodes to convert stator current (ac) to direct current (dc)
Full-wave rectification
  Changes both positive and negative polarities into direct current

## Slide 17: Alternator Rectifier (Cont.)
Diode trio
  Supply current to rotor field windings
Rectifier diodes mounted in diode frame or heat sink
  Three positive diodes press-fit in insulated frame
  Three negative diodes mounted in uninsulated or grounded frame

## Slide 18: Rectifier Assembly
(Ford)

## Slide 19: Alternator Components (Cont.)
Alternator stator
  Three sets of windings, each wrapped around laminated iron core
Alternator fan
  Mounted on front of rotor shaft
Alternator pulley
  Uses a belt to spin rotor

## Slide 20: Voltage Regulator
Control alternator output by changing current flowing through rotor’s field windings
Integral voltage regulator
  Mounted inside or on alternator rear
  Most common type used on today’s vehicles

## Slide 21: Voltage Regulator Operation
To increase alternator output
  Allows more current into rotor’s field windings
To reduce alternator output
  Places more resistance between battery and field windings
Alternator speed and electrical load determine whether regulator increases or decreases charging output

## Slide 22: ECM Charging System Monitoring and Control
Control module can monitor charging system output and react to changing operating conditions
Computer controls duty cycle of alternator’s field
  Duty cycle is percentage of time current feeds to alternator’s field windings
    50% duty cycle is normal

## Slide 23: Battery Thermistor/Fail-Safe Circuit
Battery thermistor
  Measures battery temperature so charging system can alter charging output as needed
Fail-safe circuits
  Disconnect alternator output if voltage levels become too high

## Slide 24: Alternator Drive Belts
Powered by crankshaft pulley
Turns alternator pulley and rotor
Three belt types
  V-belt
  Cogged V-belt
  Ribbed belt
(Gates)

## Slide 25: Charge Indicators
Informs driver of operating condition or output of charging system
Three basic types
  Warning light
  Voltmeter indicator
  Ammeter indicator

## Slide 26: Alternator Warning Light
Wired into charging system
  Will glow when alternator output drops to specified level
In good charging systems, current flow through field will be too low to light bulb

## Slide 27: Voltmeter Indicator
Warns driver of charging system problems
Simply shows voltage
Indicator of current output and charging system condition
If reading is too high, overcharging can occur
  When excess current is forced through battery

## Slide 28: The Charging Circuit

## Slide 29: Hybrid Charging Systems
Many hybrid vehicles do not have conventional alternators
Motor-generator recharges high-voltage battery or conventional 12-volt battery

## Slide 30: Hybrid Charging System Parts
Major parts of hybrid charging system
Motor-generator
Hybrid instrumentation
HV power control module
HV battery
Hybrid control module

## Slide 31: Hybrid Charging System Components
(Audi)