## Slide 2: 33
Charging System Diagnosis, Testing, and Repair
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Inspect a 12-volt and high-voltage (HV) charging system to locate obvious troubles.
Diagnose 12-volt and HV charging system troubles.
Test 12-volt charging system with a voltmeter, load tester, and scope.

## Slide 4: Objectives
Remove and reinstall an alternator.
Diagnose high voltage hybrid charging system problems
Correctly answer ASE certification test questions on charging system service.

## Slide 5: 12-Volt Charging System Diagnosis
12-volt charging system has only two major parts
  Alternator
  Regulator
Troubleshooting can be difficult
  Sometimes another system’s fault will appear to be caused by charging system problems
  Bad starting motor, defective battery, computer failure, or faulty wiring

## Slide 6: 12-Volt Charging System Diagnosis (Cont.)
There are four common symptoms
Dead battery
Overcharged battery
Abnormal noises
Indicator shows problem

## Slide 7: Preliminary Inspection
Visually inspect charging system parts
Check for battery-related problems
  Loose battery cables
  Discharged battery
  Corroded terminals
  Low water level
  Damaged battery case
Make sure belt tension is adjusted to specifications

## Slide 8: Preliminary Inspection (Cont.)
Check condition of alternator drive belt
Look for
  Cracks
  Glazing
  Grease
  Oil contamination
  Deterioration

## Slide 9: Preliminary Inspection (Cont.)
Check for
  Loose or corroded electrical connections
  Shorted wires
  Missing insulation
  Wiring problems
  Check electrical connections on back of alternator
Wiggle wiring harness from alternator to firewall or ECM while engine is running

## Slide 10: Preliminary Inspection (Cont.)
With engine running, listen closely for abnormal noises
Use stethoscope to listen for
  Dry, noisy alternator bearings
  Grinding
    Worn, dry bearings
  Whining
    Leaking diodes or overcharging
  Any other unusual sounds

## Slide 11: Scanning 12-Volt Charging Systems
Connect scan tool to aid in troubleshooting
Scan tool will display
  Charging voltage
  Battery temperature
  Other data useful in finding problems
Capabilities vary with each model

## Slide 12: 12-Volt Charging System Precautions
Disconnect battery before removing any charging system component
Disconnect battery before connecting it to charger
Never reverse polarity
  Connecting battery or jumper cables backward can lead to serious electrical damage

## Slide 13: 12-Volt Charging System Precautions (Cont.)
Do not operate alternator with output wire disconnected
Never short or ground any charging system terminal
  Unless instructed to do so by shop manual

## Slide 14: 12-Volt Charging System Tests
Scan tool test
Load test
Scope tests
Voltmeter test
Circuit resistance tests

## Slide 15: Scan Tool Test
To access alternator charging voltage with scan tool or diagnostic tablet
Start and idle engine
Turn on all electrical accessories to load alternator
Use scan tool to access data stream values
Scroll alternator to alternator or charging system live voltage readings
Output of at least 13 volts indicates normal operation
Below 12.6 volts indicates alternator is bad

## Slide 16: Load Test
Connect tester leads, as described by manufacturer
Clip inductive amps pickup around insulation on negative battery cable
Set load tester controls to proper positions and values
Attach vent hose to exhaust and start engine

## Slide 17: Load Test (Cont.)
Rotate load control on tester until ammeter displays alternator’s rated amperage
  Do not exceed alternator’s output rating in amps
  Do not let voltage drop below full battery voltage of 12.6 volts
Note alternator output current at 12.6 volts
Turn off load control and evaluate readings

## Slide 18: Scope Tests
Connect red scope test lead to alternator battery (output) terminal
Ground other scope lead
Start engine and observe scope trace (waveform)
Charging system should produce relatively smooth dc voltage trace with minimum ripple

## Slide 19: Voltmeter Test
Charge battery, if drained before testing
Set voltmeter to read low voltage
Connect voltmeter test leads across battery terminals
Measure and record battery base voltage
  Battery voltage with everything off

## Slide 20: Voltmeter Test (Cont.)
Start engine and record no-load voltage
  Engine running and electrical accessories off
  Voltmeter reading should increase from base reading, but not by more than 2–3 volts
Turn on all electrical accessories to load charging system
  Record load voltage

## Slide 21: Voltmeter Test (Cont.)
  Shows if charging system is providing current for all electrical units and still has enough current to recharge battery
Calculate charge voltage using formula
  Load voltage – base voltage = charge voltage

## Slide 22: VOM Test
(Fluke)

## Slide 23: Circuit Resistance Tests
Locate wiring problems in charging system
  Loose connections
  Corroded terminals
  Partially burned wires
Perform resistance tests when symptoms point to problems other than alternator or regulator

## Slide 24: Insulated-Circuit Resistance Test
Connect tester across alternator output terminal and positive battery terminal
With vehicle running at fast idle, set load control to obtain 20 amp current flow
  All lights and accessories should be off

## Slide 25: Insulated-Circuit Resistance Test (Cont.)
If circuit is in good condition, voltmeter should not read over about 0.7 volts
  0.1 volt per electrical connection
If voltage reading is higher than 0.7 volts, circuit resistance is high and poor connection exists in that charging circuit section

## Slide 26: Ground-Circuit Resistance Test
Similar to insulated-circuit resistance test
Voltmeter is placed across negative battery terminal and alternator housing
Voltmeter should not read over 0.1 volt per electrical connection
If voltmeter reads higher, look for
  Corroded or loose connections
  Burned plug socket
  Damaged wiring harness

## Slide 27: Voltage Drop and Resistance Tests

## Slide 28: Alternator Service
Bad alternators show up in tests as low output or unclean dc problem
Most shops replace alternators that exhibit these symptoms

## Slide 29: Alternator Removal
Disconnect battery to prevent major electrical short and wiring harness fire
Remove alternator belt off its drive pulley
Disconnect wiring harness from rear of alternator
Remove bolts that secure alternator
Remove alternator wires

## Slide 30: Alternator Removal (Cont.)
(Mazda)

## Slide 31: Alternator Rebuild
Alternator rebuild typically involves
Disassembling alternator
Inspecting and testing rotor
Inspecting and testing stator
Testing diodes
Replacing rotor, stator, or diodes if they are defective
Replacing bearings
Replacing brushes
Reassembling and testing alternator

## Slide 32: Alternator Installation
With battery still disconnected, fit alternator onto front of engine
Install mounting bolts
Torque to specifications
Reconnect wiring harness
Check alternator belt condition
  Replace if needed
Slip belt over engine and alternator pulley, making sure it aligns properly on each pulley

## Slide 33: Hybrid Charging System Service
HV power control module (HV PCM) generates different voltage levels for various vehicle electrical systems
  13–15 volts dc for conventional circuits
  45–110 volts dc for heated windshield circuits
  High voltage for recharging HV battery
Check dash instrumentation to verify proper operation

## Slide 34: Hybrid Charging System Service
(Toyota)

## Slide 35: Scanning Hybrid Charging Systems
Most common problems with HV charging system
Bad HV PCM
Bad motor-generator
Failed hybrid control module
Loose or corroded HV power cables
Bad HV battery