## Slide 2: 40
Fuel Tanks, Pumps, Lines, and Filters
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Define the major parts of a fuel supply system.
Describe the operation of mechanical and electric fuel pumps.
Explain the tests used to diagnose problems with fuel pumps, fuel filters, and fuel lines.
Repair a fuel line or replace a fuel hose.

## Slide 4: Objectives
Locate and replace fuel filters in both gasoline and diesel fuel systems.
State safety rules for working on fuel supply systems.
Describe the construction and action of air filters.
Correctly answer ASE certification test questions on fuel tanks, fuel pumps, fuel lines, fuel filters, and air filters.

## Slide 5: Fuel Tanks, Pumps, Lines, and Filters Introduction
Fuel system
  Provides combustible air-fuel mixture to power engine
This chapter explains construction, operation, and service of fuel tanks, fuel lines, fuel filters, air filters, and fuel pumps

## Slide 6: Fuel System Technology
Utilizes three subsystems
Fuel supply system
  Provides clean, filtered gasoline, diesel oil, or alternate fuel to fuel injectors
Air supply system
  Allows clean, filtered, air to flow into combustion chambers
Fuel metering system
  Meters correct amount of fuel into engine cylinders

## Slide 7: Fuel Supply System
Fuel tank
  Stores gasoline, diesel fuel, gasohol, alcohol, LPG, or other combustible material safely
Fuel lines
  Carry fuel between fuel tank, fuel pumps, fuel hoses, fuel filters, pressure regulator, and other system parts

## Slide 8: Fuel Supply System (Cont.)
Fuel pumps
  Draw fuel from tank and force it to engine and fuel injectors
Fuel filters
  Remove contaminants such as water, rust, and other debris

## Slide 9: Fuel Supply System Components
(Honda)

## Slide 10: Fuel Tanks
Safely hold supply of fuel so vehicle can be driven reasonable distance without refueling
Mounted in rear of car, under trunk or rear seat
Driving range
  Driving distance without stopping for fuel
Fuel tank capacity
  Volume of fuel a fuel tank can hold
  Average 12–25 gallons or 45–95 liters

## Slide 11: Fuel Tank Construction
(Chrysler)

## Slide 12: Fuel Tank Construction (Cont.)
Made of sheet steel, aluminum, or injection molded plastic
Filler neck
  Extension tube that allows gas pump nozzle to be used to fill tank with fuel
Filler cap
  Fits on end of filler neck

## Slide 13: Fuel Tank Construction (Cont.)
Spillback ball
  Large “ping pong-type” ball in filler neck to prevent fuel from leaking out of vehicle
Fuel tank baffles
  Located inside fuel tank to keep fuel from sloshing, or splashing, around
Fuel tank straps
  Secure tank to vehicle

## Slide 14: Fuel Tank Construction (Cont.)
Pickup-sending unit
  Extends down into tank to draw out fuel and operate fuel gauge
  Variable resistor
    Resistance changes with changes in fuel level
Fuel tank pressure sensor
  Monitors buildup pressure in late-model vehicles equipped with OBD II systems

## Slide 15: Fuel Tank Pickup-Sending Unit

## Slide 16: Fuel Lines and Hoses
Fuel hoses
  Carry fuel from tank to engine
Fuel rail
  Large-diameter fuel line feeding to inlet openings of fuel injectors
Hose clamps
  Secure hoses to fuel lines or metal fittings

## Slide 17: Fuel Lines and Hoses (Cont.)
Plastic fuel lines or fuel pipes
  Made of high-strength nylon tubing
  Withstand chemical action, pressure, and heat of fuel system applications
Fuel return system
  Cools gasoline and prevents vapor lock
    Bubbles form in overheated fuel and stop fuel flow
    Keeps engine heat from overheating gasoline

## Slide 18: Returnless Fuel Injection Systems
Returnless fuel injection systems
  No fuel return lines
Help reduce evaporative emissions by minimizing fuel vaporization
Control fuel system pressure by varying fuel pump output

## Slide 19: Fuel Filters
Stop contaminants
Sand, dirt, water
Rust
Corrosion
Damage
Fuel pump
Fuel lines
Pressure regulator
Fuel rail
Injectors

## Slide 20: Fuel Filters (Cont.)
Pleated fuel filter
  Made of coated paper or plastic
  Most common fuel filter element found in gasoline fuel systems
Bowl fuel filter
  Found on modern diesel engines
  Easily trap water since water is heavier than fuel

## Slide 21: Fuel Filters (Cont.)
Canister fuel filter
  Housed inside metal container
  Mounted in fuel line
Fuel strainer or soft metal sock
  Inlet of in-tank fuel pump
  Keeps debris from entering system

## Slide 22: Fuel Filter Locations
In fuel tank at end of fuel pickup tube
In fuel line before fuel rail, fuel injectors, diesel injection pump, or carburetor
Inside fuel pump
In fuel line right after electric fuel pump
Under fuel line fitting in antique carburetors

## Slide 23: Fuel Pumps
Draw fuel out of tank and force it into engine under pressure
Many engines use two fuel pumps
One in tank and one in fuel line
Connected in series using fuel hoses and metal fuel lines
(Bosch)

## Slide 24: Mechanical Fuel Pumps
Powered by engine camshaft eccentric
  Egg-shaped lobe
Produces reciprocating motion on piston or plunger
Classified as reciprocating pump

## Slide 25: Mechanical Fuel Pump Check Valves
Two check valves
Inlet check valve
Outlet check valve
Fuel flows easily through valves in one direction
Cannot flow through in other direction

## Slide 26: High-Pressure Mechanical Fuel Pump Operation
Fuel pump pressure stroke
  Eccentric lobe pushes on fuel pump rod and plunger
  Pressure pushes fuel past outlet check valve
Fuel pump charging stroke
  Eccentric lobe rotates away from fuel pump
  Pumping chamber refills with fuel from tank

## Slide 27: Fuel Pump Pressures
Mechanical fuel pump pressures can range from 1500–2000 psi
Enough pressure to cause serious injury
If it ignites and burns
    Like a large blow torch
If it does not ignite
  Puncture skin
  Inject gasoline into bloodstream
    Could be fatal

## Slide 28: Electric Fuel Pumps
Produces fuel pressure and flow for fuel metering section
Located in fuel tank or in series with fuel line
In many late-model vehicles, tank sending unit is integral part of in-tank fuel pump assembly

## Slide 29: Electric Fuel Pumps (Cont.)
Electric pumps produce almost instant fuel pressure
Rotary-type pumps produce smoother flow of fuel
Pressure ranges from 10–50 psi
(Honda)

## Slide 30: Rotary Fuel Pumps
Rotary fuel pump types include
  Impeller
  Roller vane
  Sliding vane
All use circular, or spinning, motion to produce pressure

## Slide 31: Rotary Fuel Pumps (Cont.)
Impeller electric fuel pump
  Centrifugal pump
  located inside the fuel tank
  Uses small dc motor to spin impeller
Roller vane electric fuel pump
  Positive displacement pump
  Each pump rotation moves specific amount of fuel
  Located in main fuel line

## Slide 32: Rotary Fuel Pumps (Cont.)
Sliding vane electric fuel pump
  Similar to roller vane pump
  Square vanes instead of round rollers
Reciprocating electric fuel pump
  Same basic action as mechanical fuel pump
  Uses solenoid instead of rocker arm to produce pumping motion

## Slide 33: Electric Fuel Pump Circuits
Must send controlled amount of current to pump motor
Inertia switch circuit
  Cuts electric fuel pump power in event of serious auto collision or accident
Oil pressure switch
  Safety feature that shuts off fuel pump if oil pressure is low

## Slide 34: Typical Electric Fuel Pump Circuit
(Ford)

## Slide 35: Fuel Supply System Service
Fuel supply system scanning
  Scan for trouble codes before starting fuel supply system repairs
OBD II systems
  Monitor fuel tank pressure, fuel line pressure, fuel level, and other conditions
Scan tool
  Quickly finds any stored codes
  Displays operating values for electrical circuit, and speeds troubleshooting

## Slide 36: Fuel Supply System Service (Cont.)
Vapor lock
  When bubbles in overheated fuel reduce or stop fuel flow
Fuel tank problems
  Fuel leakage
  Physical damage
    Dents, holes, etc.
Contamination
  Rust, dirt, and water

## Slide 37: Fuel Tank Removal and Replacement
Before servicing a fuel tank, empty it
  Full tank is very heavy and can rupture if dropped
  Drain fuel into approved safety can
Disconnect hose at main fuel line and route it into approved gas can
Turn ignition key on
Allow fuel pump to force fuel from tank into can

## Slide 38: Fuel Tank Removal and Replacement (Cont.)

## Slide 39: Fuel Tank Removal and Replacement (Cont.)
After draining, remove tank from vehicle
Disconnect filler neck, fuel lines, wires, and other components
Remove straps or bolts securing tank to body
Slowly and carefully lower tank
Remove old electric fuel pump and sending unit assembly from bad fuel tank

## Slide 40: Fuel Tank Removal and Replacement (Cont.)
Install fuel pump into new tank
Use rubber O-ring to make sure new fuel tank does not leak
If working alone
  Secure fuel tank on transmission jack and raise it up under vehicle
Make sure to replace rubber insulators
Check that all fuel lines are properly secured
Replace fuel in tank and check for leaks

## Slide 41: Fuel Tank Sending Unit Service
Faulty fuel tank sending unit can make fuel gauge reading inaccurate
Usually, variable resistor in sending unit fails
Sometimes fuel gauge or gauge circuit may be at fault

## Slide 42: Fuel Tank Sending Unit Service (Cont.)
First, test fuel gauge
  Connect factory fuel gauge tester to fuel gauge feed wire
  When tester is set on full
    Fuel gauge should read full
If gauge does not function
  Either gauge or gauge circuit is faulty
If fuel gauge begins to work
  Fuel tank sending unit is bad

## Slide 43: Fuel Tank Sending Unit Service (Cont.)
If tests indicate inoperative fuel tank sending unit, remove unit after draining tank
Unscrew cam lock or screws holding sending unit in fuel tank
If without special cam tool, use drift punch and hammer to rotate lock tabs
Lift unit out of tank

## Slide 44: Fuel Tank Sending Unit Service (Cont.)
Measure resistance with ohmmeter
If resistance is not within specifications
  Or does not change when float arm moves
Install new sending unit
Also check float for leakage
(Honda)

## Slide 45: Fuel Line and Hose Service
Faulty fuel lines and hoses are common sources of fuel leaks
Fuel hoses can become hard and brittle
Engine oil softens and swells hoses
Inspect fuel lines and hoses closely
Replace any in poor condition

## Slide 46: Fuel Line and Hose Service Rules
Wear proper apparel
  Work gloves and eye protection
Release residual fuel pressure
Place shop rag around fuel line fitting during removal
Only use approved double-wall steel tubing for fuel lines

## Slide 47: Fuel Line and Hose Service Rules (Cont.)
Make smooth bends when forming new fuel line
Form double-lap flares on ends of fuel line
Reinstall fuel line hold-down clamps and brackets
Route all fuel lines and hoses away from hot or moving parts

## Slide 48: Fuel Line and Hose Service Rules (Cont.)
Route plastic fuel lines in their original locations
Plastic line will kink if bent too sharply
Use factory-recommended tool to release snap-type fittings used to secure plastic fuel lines
If plastic line or fitting is damaged, replace it

## Slide 49: Fuel Line and Hose Service Rules (Cont.)
Do not use non-OEM plastic tubing to repair fuel systems
Plastic lines tend to stiffen in service
  Avoid bending or rerouting used plastic lines
Always cover plastic fuel lines with wet towel when welding, torch cutting, or grinding near them

## Slide 50: Fuel Line and Hose Service Rules (Cont.)
Never allow battery acid to contact metal or plastic fuel line
Use only approved synthetic rubber hoses in fuel system
Make sure fuel hose fully covers its fitting or line before installing clamps

## Slide 51: Fuel Line and Hose Service Rules (Cont.)
When servicing press-fit fuel line fittings, O-ring seal may need replacing to prevent fuel leakage
Double-check all fittings for leaks
Start engine and inspect connections closely

## Slide 52: Fuel Filter Service
Involves periodic replacement or cleaning of system filters
  May also include locating clogged fuel filters
Partially clogged fuel filter may cause engine to temporarily lose power or stall when specific speed is reached
Clogged in-tank strainer is common and difficult-to-diagnose problem

## Slide 53: Fuel Pump Service
Problems include
Low fuel pressure
Inadequate fuel flow
Abnormal pump noise
Fuel leakage

## Slide 54: Fuel Pump Service (Cont.)
Low fuel pump pressure causes
  Worn pump bearings
  High resistance in electric pump circuit
  Leaking check valves
  Physical wear of moving parts
With low fuel pump pressure, engine starves for fuel at high speeds

## Slide 55: Fuel Pump Service (Cont.)
High fuel pump pressure is commonly caused by inoperative pressure relief valve
  Faulty fuel pressure regulator is another cause
Mechanical fuel pump noise
  Clacking sound from inside pump
  Caused by weak or broken return spring or other pump part failure

## Slide 56: Fuel Pump Tests
Fuel pump testing
  Measuring fuel pump pressure and volume
Exact procedures vary, depending on fuel system type
Refer to manual
Sometimes, fuel pump vacuum is measured to find air leaks in fuel supply lines

## Slide 57: Fuel Pump Tests (Cont.)
Before testing fuel pump, use scan tool to check for
Restricted fuel filters
Smashed or kinked fuel lines or hoses
Air leak into vacuum side of pump or line
Injection system troubles
Ignition system problems
Low engine compression

## Slide 58: Measuring Fuel Pump Pressure
Relieve any residual pressure in system
Connect pressure gauge to output line of fuel pump
  Or test fitting on engine fuel rail
    May need to install test fitting in fuel line
If mechanical fuel pump, start engine
Inspect all test fittings for leakage
Compare pressure readings with specifications

## Slide 59: Measuring Fuel Pump Pressure (Cont.)
To test electric fuel pump
Activate electric pump motor
Press hybrid start button, or start engine
Compare pressure readings to specifications
(Chrysler)

## Slide 60: Measuring Fuel Pump Pressure (Cont.)
Fuel pressure for gasoline injection system can vary from 50–2000 psi
Diesel supply pump should produce around 10–15 psi
Old carburetor-type fuel systems should be very low, about 4–6 psi
Older fuel-injected vehicles may run 30–50 psi

## Slide 61: Measuring Fuel Pump Volume
Route output line from fuel pump into graduated container
  For safety, use valve or clip to control fuel flow into container
With engine idling at specified speed, allow fuel to pour into container for prescribed amount of time
  Normally 30 seconds
Close off clip or valve, and shut off engine
Compare volume output to specifications

## Slide 62: Measuring Fuel Pump Volume (Cont.)
Fuel pump volume or fuel pump capacity
  Fuel amount pump can deliver in specific amount of time
Fuel pump volume output should be minimum of one pint in 30 seconds for small automobile engines
  Larger engines will require slightly higher fuel volume output

## Slide 63: Measuring Fuel Pump Vacuum
Should be checked when fuel pump fails pressure and volume tests
Connect vacuum gauge to inlet side of pump
Leave fuel hose, from volume test, in graduated container
Open valve and activate pump
Compare vacuum reading to specifications
  Fuel pump vacuum should be about 7–10" Hg

## Slide 64: Electric Fuel Pump Circuit Tests
Many electric fuel pump problems caused by circuit problems
  Broken wires, bad relays, shorts, blown fuses, computer malfunctions, and other troubles affect operation
Measure supply voltage being fed to pump motor
  If voltage is low, problem is in electrical circuit to pump

## Slide 65: Fuel Pump Shutoff Circuits
Inertia switch
  Blocks current flow to electric fuel pump after severe impact or collision
  After collision, you must press a button on switch before pump will function again

## Slide 66: Fuel Pump Shutoff Circuits (Cont.)
Low oil pressure safety circuit
  Protect engine from major mechanical damage
  Signals ECM to shut off electric fuel pump if engine oil pressure drops too low

## Slide 67: Mechanical Fuel Pump Replacement
Disconnect battery to keep electric sparks from starting fuel fires
  On hybrid, also disable HV battery
Following factory service manual procedures, relieve any residual fuel pressure
Use tubing wrenches to disconnect fuel lines going to fuel pump

## Slide 68: Mechanical Fuel Pump Replacement (Cont.)
Unbolt pump from engine
Compare old mechanical pump with new one to make sure identical
Scrape off any remaining gasket material on engine cylinder head or front cover

## Slide 69: Mechanical Fuel Pump Replacement (Cont.)
If used, install new gasket or seal on new fuel pump
Fit fuel pump onto its mount and hand start fuel pump bolts or nuts
Torque fuel pump bolts to exact specifications

## Slide 70: Electric Fuel Pump Replacement
With inline pump, disconnect fuel fittings and remove pump
Usually, in-tank pump must be removed as part of tank pickup-sending unit
  Procedure described earlier in chapter

## Slide 71: Air Filter Service
Air filter or air cleaner
  Removes foreign matter from air entering engine intake manifold
Element
  Filter element fits inside metal or plastic housing
When replacing filter element, clean out filter housing
(Ford)