## Slide 2: 48
Cooling System Testing, Maintenance, and Repair
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
List common cooling system problems and their symptoms.
Describe the most common causes of system leakage, overheating, and overcooling.
Perform a combustion leak test and a system pressure test.
Check the major parts of a cooling system for proper operation.

## Slide 4: Objectives
Replace faulty cooling system components.
Drain, flush, and refill a cooling system.
Describe safe working practices to use when testing, maintaining, or repairing a cooling system.
Correctly answer ASE certification test questions on cooling system troubleshooting and repair.

## Slide 5: Cooling System Testing, Maintenance, and Repair Introduction
Excess heat causes engine damage
Melted pistons
Cracked or warped cylinder heads
Burned exhaust valves
Burned or “blown” head gaskets
Damaged radiator and heater hoses
Cracked engine exhaust manifolds
Cracked or warped plastic intake manifolds

## Slide 6: Cooling System Troubleshooting
Can you describe the cooling system problem?
  Temperature light on, overheating, visible steam, or coolant loss
When does the problem seem to occur?
  All the time, at highway speeds, when idling, in all-electric mode, when engine starts, when engine is hot or cold
When did the problem begin?

## Slide 7: Cooling System Troubleshooting (Cont.)
Have any other engine or electric powertrain repairs been performed?
Have you noticed any coolant leaks?
  If so, where are leaks located?
Are there any unusual noises that might be related to the cooling system?
  Engine grinding, hissing of steam, HV electrical humming

## Slide 8: Cooling System On-Board Diagnostics
Trouble codes trip when circuits operate out of range
Engine cooling
Transmission cooling
Motor-generator cooling
Power control circuit cooling for electric drive train

## Slide 9: Cooling System On-Board Diagnostics (Cont.)
Circulation of air and coolant required to keep mechanical and electronic systems working properly
Vehicle diagnostic systems monitor coolant and air temperatures in all systems that generate high heat levels

## Slide 10: Diagnosis Charts
Cooling system diagnosis chart
  Use when problems are difficult to locate
Contain very accurate chart for particular design and type of engine and cooling system

## Slide 11: Cooling System Inspection
Trouble Signs
Coolant leaks
Loose or missing fan belt
Low coolant level
Abnormal water pump noises
Leaves and debris covering outside of engine radiator
Coolant in oil
Combustion leakage into engine coolant

## Slide 12: Cooling System Problems
Coolant leaks
  Cracks or ruptures in system allow pressure cap action to push coolant out of system
Overheating
  When engine operating temperature is too high
Overcooling
  Engine fails to reach full operating temperature

## Slide 13: Combustion Leak Test
Checks for presence of combustion gases in coolant
Place block and head tester in radiator filler neck or reservoir
Start engine
Squeeze and release tester bulb
  This will pull air from cooling system through tester

## Slide 14: Combustion Leak Test (Cont.)
Fluid in block tester is normally blue
Chemicals in exhaust gases react in test fluid, changing its color
Combustion leak will turn fluid yellow
If fluid remains blue, no combustion leakage

## Slide 15: Coolant in Oil
When water, antifreeze, and oil mix, solution turns milky white in color
Milky white solution found in engine oil or in valve covers, indicates coolant leak

## Slide 16: Cooling System Pressure Test
Quickly locates leaks in radiator, water pumps, hoses, engine, or HV component
Disconnect or disable battery for safety
Make sure cooling system has had enough time to cool down before opening system to release pressure
Slowly remove radiator pressure cap

## Slide 17: Cooling System Pressure Test (Cont.)
Find correct size tester cap to fit radiator filler neck
Press correct test cap straight down with both hands while turning it clockwise
Make sure test cap sealed properly over both lugs on radiator filler neck
Attach hand pump to test cap on cooling system radiator

## Slide 18: Cooling System Pressure Test (Cont.)
Pump maximum rated pressure into system by pumping tester handle
Do not exceed maximum factory-rated cooling system pressure or you could cause damage
Use shop light to inspect for coolant leakage around and under engine or major hybrid cooling system parts

## Slide 19: Cooling System Pressure Test (Cont.)
With pressure in system, inspect all parts for coolant leakage
  Check all hose fittings, gaskets, and engine freeze plugs
  Look under water pump and around radiator
If coolant leak is found, tighten, repair, or replace parts and gaskets, as needed

## Slide 20: Radiator Cap Pressure Testing
Make sure system is not under pressure
Carefully remove radiator cap
  Inspect cap and filler neck sealing surfaces
Install radiator cap on pressure tester using adapter
Pump tester to pressurize cap
  Cap should release air when rated pressure is exceeded

## Slide 21: Causes of Engine Overheating
Low coolant level
Rust or scale
Stuck thermostat
Retarded ignition timing
Loose fan belt
Bad water pump
Collapsed lower hose
Missing fan shroud
Ice in coolant
Engine fan problems
Open temperature sensor

## Slide 22: Causes of Cooling System Overcooling
Conditions that cause cooling system overcooling
Thermostat stuck open
Thermostat stuck closed
Locked fan clutch
Shorted fan switch
Shorted temperature sensor

## Slide 23: Water Pump Service
Bad water pumps
Leak coolant
  Worn seal
Fail to circulate coolant
  Broken shaft or damaged impeller
Produce grinding sound
  Faulty pump bearings
Rust in cooling system and lack of coolant are common reasons for pump failure

## Slide 24: Checking a Water Pump
Check for bad water pump seal
  Pressure test system and watch for leakage at pump
  Leaking water pump must be replaced
If pump shaft is loose in its housing, pump bearings are badly worn
  Pump replacement is usually necessary

## Slide 25: Removing a Water Pump
Make sure cooling system is not under pressure and battery is disconnected
Carefully remove radiator cap
Place drain pan under radiator
Open drain valve
Allow radiator to completely drain
Close drain valve

## Slide 26: Removing a Water Pump (Cont.)
Remove fan belt(s)
Unbolt all brackets and other components preventing pump removal
Remove radiator hose(s) from water pump
Remove bolts holding water pump to engine

## Slide 27: Removing a Water Pump (Cont.)
Make sure all bolts are out and lightly tap rear or side of pump housing with mallet to free pump
Scrape off all old gasket or sealer material from engine

## Slide 28: Installing a Water Pump
Install water pump gasket
  Use approved sealer to adhere new gasket to pump
Use chemical gasket
  Apply 1/8″ continuous bead around pump sealing surface
If water pump uses O-ring seal, work new seal down into bottom of groove in pump or engine

## Slide 29: Installing a Water Pump (Cont.)
Fit pump onto engine and move it straight into place
  Do not shift gasket or break sealant bead
Start all bolts by hand
  Screw them in two turns
  Check that all bolt lengths are correct

## Slide 30: Installing a Water Pump (Cont.)
Tighten all fasteners to 1/2 of full torque in crisscross pattern
Tighten all fasteners to 3/4 of full torque in crisscross pattern
Tighten all fasteners to full torque in crisscross pattern
Tighten all fasteners to full torque one more time to ensure proper torque

## Slide 31: Installing a Water Pump (Cont.)
Reinstall hose(s) onto water pump
Reattach any removed brackets or components
Reinstall fan belt(s), as needed
Fill radiator with coolant
Start engine and look for leaks
Verify coolant flow through radiator
Install radiator cap

## Slide 32: Thermostat Service
Stuck thermostat can cause engine overheating or sometimes engine overcooling
Stuck shut
  Very little coolant will circulate through radiator
Stuck open
  Too much coolant may circulate through radiator

## Slide 33: Thermostat Testing
Watch coolant through opening in radiator neck (if provided)
When engine is cold, coolant should not flow through upper area of radiator
When engine warms, thermostat should open and coolant should circulate past opening in top of radiator
If coolant does not start circulating and engine overheats, thermostat is bad

## Slide 34: Thermostat Replacement
Thermostat housing
  Pot metal, aluminum, or plastic enclosure that holds thermostat in place
Remove thermostat by unbolting thermostat housing
(Toyota)

## Slide 35: Thermostat Removal
Make sure cooling system is not under pressure
Carefully remove radiator cap
Place drain pan under radiator
Remove upper radiator hose by loosening its clamp
  Pull and twist on hose to free it from thermostat housing

## Slide 36: Thermostat Removal (Cont.)
Remove any wiring connector or vacuum hose going to thermostat housing
Remove bolts holding thermostat housing to engine
  Note any difference in bolt lengths
Lift off housing
  May have to tap housing free with rubber or plastic mallet

## Slide 37: Thermostat Removal (Cont.)
Insert rag into housing and scrape all old gasket material off thermostat housing and sealing surface on engine
Make sure thermostat housing is not warped
  If warped, file or sand surface flat to prevent coolant leakage
Wipe all engine and housing mating surfaces clean with shop towel

## Slide 38: Thermostat Installation
Make sure temperature rating of new thermostat is correct
Install any O-ring into its groove in engine or thermostat housing
Normally, rod (pointed end) on thermostat should face radiator hose and away from inside of engine

## Slide 39: Thermostat Installation (Cont.)
Position new gasket with approved sealer
Slowly torque thermostat housing bolts to specifications in crisscross pattern
Fill radiator with coolant
Start engine and check for leaks
Verify that no coolant flows in radiator while engine is cool

## Slide 40: Thermostat Installation (Cont.)
Verify coolant flow through radiator once engine reaches operating temperature
Reinstall radiator cap
Once pressure builds in cooling system, check again for leaks

## Slide 41: Thermostat Installation (Cont.)
(Honda)

## Slide 42: Bleeding the Cooling System
Cooling system bleed screw or bleed valve
  Sometimes provided to help remove trapped air when refilling cooling system
Fill system with coolant
Start engine and warm to full operating temperature
Crack open bleed screw until all air is purged from system, and coolant leaks from valve

## Slide 43: Bleeding the Cooling System (Cont.)
After system cools again, remove radiator cap
Coolant level should be at top of filler neck
  If not, add coolant
Install radiator cap
Watch for coolant leaks until engine warms to full operating temperature again

## Slide 44: Cooling System Hose Service
Inspect radiator and heater hoses
  Cracks
  Bulges
  Cuts
  Any sign of deterioration or damage
Squeeze hoses to check whether hardened or softened
Replace affected hoses

## Slide 45: Coolant Hose Replacement
Make sure cooling system is not under pressure
Remove radiator cap slowly and carefully
Place drain pan under radiator
Open drain valve
  Allow coolant to flow into drain pan until empty
  Close drain valve
Loosen hose clamps

## Slide 46: Coolant Hose Replacement (Cont.)
Pull hose off fitting
  May need to cut slit in old hose to aid removal
Clean metal hose fittings with scuff pad
If corroded, coat metal hose fittings with non-hardening sealer
Apply new hose onto fitting
Position hose clamps so fully over metal hose fitting

## Slide 47: Coolant Hose Replacement (Cont.)
Tighten clamps just enough to prevent coolant leakage
Fill cooling system with antifreeze
Replace radiator cap
Inspect for coolant leaks as engine warms, or perform leak test

## Slide 48: Freeze Plug Service
Drive drift or large full-shank screwdriver through plug
Pry plug sideways without scraping engine block or cylinder head
Pop core plug out by pushing on backside of plug with pry bar
Sand core plug hole in engine by hand with 120 grit sandpaper

## Slide 49: Freeze Plug Service (Cont.)
Wipe off sealing surface with clean towel
Coat and plug the plug hole with non-hardening sealer
Drive new freeze plug squarely into position
Expansion freeze plugs are available for tight quarters

## Slide 50: Radiator Service
When tests reveal that radiator is leaking, it must be removed for service
Most radiator repair work performed in specialized radiator repair shops
Radiator in many late-model vehicles designed to be replaced rather than rebuilt

## Slide 51: Radiator Removal and Installation
Disconnect battery to prevent engine starting or shorting wires
Make sure cooling system has cooled down and is not under pressure
Carefully remove radiator cap to relieve any residual pressure
Drain all coolant from system into catch pan

## Slide 52: Radiator Removal and Installation (Cont.)
Loosen radiator hose clamps and pull off radiator hoses and oil cooler lines
Unplug any sensor wiring
  Radiator tanks
  Electric cooling fans
Remove all fasteners holding radiator to its supports and to vehicle
Carefully lift out radiator

## Slide 53: Radiator Removal and Installation (Cont.)
(Honda)

## Slide 54: Radiator Repair
Radiator shops have facilities to properly disassemble, repair, reassemble, and pressure test any radiator
Special cleaning tanks for loosening and removing scale built up inside radiator
Also remove tanks and solder in new core, if needed

## Slide 55: Engine Fan Service
Faulty engine fan can cause
  Overheating
  Overcooling
  Vibration
  Water pump damage
Check fan for
  Bent blades
  Cracks
  Other problems

## Slide 56: Electric Fan Service (Cont.)
Most electric cooling fans controlled by heat-sensitive switch or sensor located somewhere in cooling system
Many now controlled by engine ECM and temperature sensor on radiator

## Slide 57: Testing an Electric Fan
Verify that fan stays off when engine and cooling system are cool or cold
Start and idle engine
  Cooling fan(s) should begin spinning when engine reaches full operating temperature
Make sure fan motor spins at normal speed and forces air through radiator

## Slide 58: Testing an Electric Fan (Cont.)
If fan does not function when engine is warm
  Check fuse, electrical connections, fan relay, and motor supply voltage
If power is applied across fan motor windings by ECM and/or its relay, and motor fails to spin
  Fan motor needs to be replaced

## Slide 59: Testing an Electric Fan (Cont.)
If engine is warm and voltage not supplied across fan motor
  Check action of radiator temperature sensor or switching sensor with multimeter
Make sure ground circuit for fan motor has almost zero resistance

## Slide 60: Belt-Driven Fan Service
Loose fan belt will slip and squeal, and may rotate water pump and fan too slowly
  May result in engine overheating
  Loose fan belt could also fly off its pulleys
If fan belt is cracked, frayed, glazed, or oil soaked, replace it
Belt tension gauge
  Measures belt tightness

## Slide 61: Testing a Fan Clutch
Spin fan with engine off
  Fan should turn without fan shaft turning
Start engine
  When engine warms, clutch should engage
Verify that air flows through radiator and over engine

## Slide 62: Coolant Service
Coolant, or antifreeze solution, should be checked and changed at regular intervals
After prolonged use, coolant will break down and become very corrosive
Rust will form and attempt to clog small internal coolant passages in radiator and heat core

## Slide 63: Visual Coolant Inspection
Rub your finger inside radiator filler neck or reservoir tank
Check
  Rust
  Oil
    Internal engine leak
  Scale
  Transmission fluid
    Leaking oil cooler in radiator
Check coolant level during visual inspection

## Slide 64: Coolant Voltage Testing
Touch black multimeter test lead to any metal ground
Dip red multimeter test lead into coolant
Read voltage generated by coolant
Voltage of “good” coolant almost zero, or less than 0.5 volts dc when measured coolant to ground
Voltage of “bad” coolant is any reading above 0.5 volts dc

## Slide 65: Changing Coolant
When system is cool, slowly remove pressure cap
Place large, shallow catch pan under radiator
Loosen drain plug on bottom of radiator tank
Allow old coolant to drain into catch pan

## Slide 66: Changing Coolant (Cont.)
Study condition of old coolant
  If coolant is acidic or filled with rust
    Flush system before refilling it
  If coolant looks and smells okay
    Refill system
Pour old antifreeze into recycling drum
Reinstall lower radiator hose or tighten radiator drain plug

## Slide 67: Changing Coolant (Cont.)
Refill cooling system
Start and warm engine with radiator cap off
Coolant level may drop when thermostat opens
  Add more coolant until liquid stays even with filler neck

## Slide 68: Changing Coolant (Cont.)
Install radiator or reservoir cap
As engine warms and pressurizes cooling system, check for leaks at lower radiator hose and drain plug

## Slide 69: Testing Coolant Strength
Coolant strength
  Measurement of coolant’s antifreeze/water ratio
Determines freeze-up protection of coolant
Cooling system hydrometer
  Quickly measures coolant’s freezing point

## Slide 70: Testing Coolant Strength (Cont.)
Refractometer
  Another type of coolant strength measuring device seldom used anymore
Minimum coolant strength
  Should be several degrees lower than lowest normal temperature for area climate
50/50 mix of antifreeze and water commonly used to provide protection for most weather conditions

## Slide 71: Coolant Test Strips
Coolant test strips can check coolant strength and pH level
Dip reactive end of strip
Compare to test strip color key

## Slide 72: Corrosion of Aluminum
Radiators, water pumps, cylinder heads, blocks, and intake manifolds can be made of aluminum
Antifreeze designed for aluminum components must be used in these systems
Some types of antifreeze corrode aluminum

## Slide 73: Flushing a Cooling System
Flushing or cleaning
  Should be done when rust or scale is found in system
To manually flush cooling system
Drain old coolant
Add cooling system cleaning chemical to system and fill radiator with water
Replace radiator cap, start engine, and set heater controls to their hottest setting

## Slide 74: Flushing a Cooling System (Cont.)
Allow car to run for 10–15 minutes and shut it off
After allowing engine to cool, drain contents of cooling system into container
Refill system with clean water and run engine for another 10–15 minutes
Shut off engine and allow it to cool
Drain water from cooling system
Finally, refill cooling system with fresh coolant

## Slide 75: Flushing a Cooling System (Cont.)
Coolant flushing machine
  Automatically drains, flushes, and refills engine cooling system
These machines speed repair and to reduce consumption, waste, or improper disposal of antifreeze solution

## Slide 76: Temperature Gauge Service
Testing temperature gauge
Disconnect wire going to temperature gauge sending unit
  Sending unit is normally located on engine
Using jumper wire, ground gauge wire to engine block
Turn ignition key switch on and watch temperature gauge
  It will normally swing to hot when wire is grounded

## Slide 77: Temperature Gauge Service (Cont.)
Gauge tester
  Can also be used to check gauge and sending unit operation
Special testing device with variable resistor
To test temperature indicating light, set tester to specified resistance and temperature gauge should read as specified

## Slide 78: Supercharger Coolant Service
Many superchargers have separate cooling system
  Independent of engine cooling system
Service methods are the same
Supercharger cooling systems often operate at much lower pressures and temperatures
Never exceed radiator cap or reservoir pressure limits when hand-pressure-testing these systems

## Slide 79: Hybrid Cooling System Service
Hybrid cooling system service is very similar to servicing engine cooling system
Instead of belt-driven water pump, hybrid cooling systems use small electric water pump
Some hybrid battery packs have electric fan that blows air over battery packs
Other hybrid cooling systems use air and liquid cooling

## Slide 80: Hybrid Cooling System Service (Cont.)
Check
Proper coolant level in HV coolant reservoir
Obstructions of inlet and outlet air ducts to HV battery
Proper scan tool temperature readings for HV battery, HV motor-generator, and HV PCM

## Slide 81: Hybrid Cooling System Service (Cont.)
Proper operation of sensors and automatic fans that should turn on when battery current load is high
Blower motor circuit problems or mechanical problems
Leaks by performing pressure test
Acid deterioration by performing voltage test
Normal electric coolant pump operation

## Slide 82: Hybrid Cooling System Service (Cont.)