## Slide 2: 80
Brake System Technology
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Explain the hydraulic and mechanical principles of a brake system.
Identify the major parts of an automotive brake system.
Define the basic functions of the major parts of a brake system.

## Slide 4: Objectives
Compare drum and disc brakes.
Explain the operation of power brakes.
Describe the operation of parking brakes.
Correctly answer ASE certification test questions requiring a knowledge of automotive brake systems.

## Slide 5: Brake System Technology Introduction
Automotive brakes
  Provide means of using friction to either slow, stop, or hold wheels of vehicle
Moving car has tremendous amount of stored energy in form of inertia
  Tendency to keep moving
To stop vehicle, brakes convert mechanical energy into heat energy

## Slide 6: Brake System Technology Introduction (Cont.)
Hydraulic brakes
  Confined brake fluid used to transfer power and motion from brake pedal to wheel cylinders and brakes
Hybrid brakes
  Conventional hydraulic brake system combined with electric regenerative braking system provided by hybrid’s driveline

## Slide 7: Basic Brake System
Basic parts include
Brake pedal assembly
  Foot lever for operating master cylinder and power booster
Master cylinder
  Hydraulic-piston pump that develops pressure for hydraulic brake system
Brake booster
  Vacuum, electric, or power steering-operated device that assists brake pedal application

## Slide 8: Basic Brake System (Cont.)
Brake lines and hoses
  Metal tubing and rubber hose that transmit pressure to wheel brake assemblies
Wheel brake assemblies
  Hydraulic-mechanical mechanisms that use hydraulic pressure to produce friction to slow or stop each wheel
Emergency or parking brakes
  Mechanical or electric systems for applying rear brake assemblies

## Slide 9: Basic Brake System (Cont.)
(Honda)

## Slide 10: Drum and Disc Brakes
Disc brakes are frequently used on two front wheels of vehicle
Drum brakes are often used on rear wheels
Disc or drum brakes may be used on all four wheels

## Slide 11: Drum and Disc Brakes (Cont.)
Components of disc brake assembly
Caliper
  Assembly that holds hydraulic cylinder, piston, seals, and brake pads
Caliper cylinder
  Machined hole in caliper
  Piston fits into this cylinder

## Slide 12: Drum and Disc Brakes (Cont.)
Brake pads
  Friction members that push against disc by action of master cylinder, caliper cylinder, and piston
Brake disc
  Large metal rotor that holds wheel and tire and uses friction from brake pads to stop or slow wheel rotation

## Slide 13: Drum and Disc Brakes (Cont.)
Components of drum brake assembly
Wheel cylinder assembly
  Houses hydraulic piston that force outward by fluid pressure
Brake shoes
  Friction units that push against rotating brake drum by action of hydraulic wheel cylinder
Brake drum
  Rubs against brake shoes to stop or slow wheel rotation

## Slide 14: Braking Ratio
Comparison of front wheel braking effort to rear wheel braking effort
Typically, front wheel brakes handle 60%–70% of the braking power
Rear wheel brakes typically handle 30%–40% of braking
Front-wheel-drive cars can have even higher braking ratio at front wheels

## Slide 15: Brake System Hydraulics
Hydraulic system uses liquid to transmit motion or pressure from one point to another
Several principles apply to operation of hydraulic system
  Liquids in confined area will not compress
    Air in confined area will compress
  When pressure is applied to closed system, pressure exerts equally in all directions
  Hydraulic system can increase or decrease force or motion

## Slide 16: Hydraulic System Action
(OTC)

## Slide 17: Brake System Components
Know location and construction of major brake system components
This will better prepare you to troubleshoot and repair these important parts

## Slide 18: Brake Pedal Assembly
Lever arm increases force applied to master cylinder piston
Manual master cylinder bolts directly to engine’s firewall
Brake pedal assembly bolts under dash
(Bendix)

## Slide 19: Master Cylinder
Four basic functions
Develops pressure, causing wheel cylinder pistons to move toward discs or drums
After all shoes or pads produce sufficient friction, it helps equalize pressure required for braking
Keeps system full of fluid as brake linings wear
Maintains slight pressure to keep contaminants from entering system
Air and water

## Slide 20: Master Cylinder Construction
Housing
Reservoir
Piston
Rubber cup
Return spring
Rubber boot

## Slide 21: Master Cylinder Construction (Cont.)
Cup and piston
  Pressurize brake system
  When pushed forward, they trap fluid, building pressure
Intake port or vent
  Allows fluid to enter rear of cylinder as piston slides forward

## Slide 22: Master Cylinder Construction (Cont.)
Compensating port
  Releases extra pressure when piston returns to released position
  Fluid can flow back into reservoir through compensating port
Residual pressure valves
  Maintain residual fluid pressure of approximately 10 psi to help keep contaminants out of system

## Slide 23: Master Cylinder Construction (Cont.)
Rubber boot
  Prevents dust, dirt, and moisture from entering back of master cylinder
Master cylinder reservoir
  Stores an extra supply of brake fluid
  Reservoir may be cast as part of housing, or it may be removable plastic part

## Slide 24: Dual Master Cylinder
Older vehicles used single-piston, single-reservoir master cylinders
  Dangerous
If brake fluid leak developed, sudden loss of braking ability could occur
Modern vehicles use dual master cylinder for added safety

## Slide 25: Dual Master Cylinder (Cont.)
(Bendix)

## Slide 26: Dual Master Cylinder (Cont.)
Dual or tandem master cylinder
  Has two separate hydraulic pistons and two fluid reservoirs
  If there is system leak in one of hydraulic circuits, other circuit can still provide braking action on two wheels
Rear piston assembly is called primary piston
Front piston is secondary piston

## Slide 27: Dual Master Cylinder Operation
(Delco)

## Slide 28: Power Brakes
Use booster and either engine vacuum, electric pump, or hydraulic pressure to assist brake pedal application
Booster is located between brake pedal linkage and master cylinder

## Slide 29: Power Brake Vacuum Boosters
Vacuum booster
  Uses engine vacuum to apply hydraulic brake system
  Or vacuum created by separate pump on diesel engines
When vacuum is applied to one side of booster, piston or diaphragm moves toward low-pressure area
This movement helps force piston into master cylinder

## Slide 30: Vacuum Booster Types
Two types of vacuum brake boosters
Atmospheric suspended brake booster
  Has atmospheric pressure on both sides of diaphragm or piston when brake pedal is released
Vacuum suspended brake booster
  Has vacuum on both sides of piston or diaphragm when brake pedal is released

## Slide 31: Power Brake Hydraulic Boosters
Hydraulic booster, hydro-boost or hydra-booster
  Uses power steering pump pressure to help driver apply brake pedal
Fluid pressure, instead of vacuum, helps force piston forward
Commonly used on vehicles equipped with diesel engines

## Slide 32: Brake Fluid
Specially blended hydraulic fluid that transfers pressure to wheel brake assemblies
Automakers recommend brake fluid that meets or exceeds SAE and DOT specifications
  Society of Automotive Engineers
  Department of Transportation
Only use brake fluid that satisfies their requirements

## Slide 33: Brake Fluid (Cont.)
Brake fluid must have these characteristics
Maintain correct viscosity
  Free flowing at all temperatures
High boiling point
  Remains liquid at highest system operating temperature
Noncorrosive
  Does not attack metal or rubber brake system parts

## Slide 34: Brake Fluid (Cont.)
Water tolerant
  Absorbs moisture collecting in system
Lubricates
  Reduces wear of pistons and cups
Low freezing point
  Does not freeze in cold weather

## Slide 35: Brake Lines and Hoses
Transfer fluid pressure from master cylinder to wheel brake assemblies
Brake lines are made of double-wall steel tubing and usually have double-lap flares on their ends to prevent high pressure leakage

## Slide 36: Brake Lines and Hoses (Cont.)
Brake hoses are reinforced braided rubber hydraulic hoses with threaded metal end fittings
Junction block is used where single brake line must feed two wheel cylinders
  Hollow fitting with one inlet and two or more outlets

## Slide 37: Brake Lines and Hoses (Cont.)
Longitudinally split brake system
  Pistons operate front and rear
Diagonally split brake system
  Pistons operate opposite corners
(Delco)

## Slide 38: Disc Brake Assemblies
Friction elements are squeezed inward to clamp against rotating disc, or wheel
Disc brake assembly consists of caliper, brake pads, disc, and related hardware

## Slide 39: Brake Caliper
Brake caliper assembly includes caliper housing, piston, piston seal, dust boot, brake pads, special hardware, and bleeder screw
When brake pedal is applied, brake fluid flows into caliper cylinder
Piston is then pushed outward by fluid pressure, forcing the brake pads into disc

## Slide 40: Brake Caliper (Cont.)
Piston seal
  Prevents pressure leakage between piston and cylinder
Piston boot
  Keeps road dirt and water off caliper piston and wall of cylinder
Bleeder screw
  Allows air to be removed from hydraulic brake system

## Slide 41: Brake Caliper (Cont.)
(Chrysler)

## Slide 42: Disc Brake Pads
Steel plates to which linings are riveted or bonded
Each caliper has inner and outer brake pad that fits inside hydraulic brake caliper
Brake pad linings
  Made of heat-resistant organic or semimetallic friction material

## Slide 43: Disc Brake Pads (Cont.)
Anti-rattle clips
  Keep brake pads from vibrating and rattling
  Snap onto brake pad to produce force fit in caliper
Pad-wear sensor
  Metal tab on brake pad that informs driver of worn brake pad linings

## Slide 44: Brake Disc
Brake disc or brake rotor
  Uses friction from brake pads to slow or stop wheel rotation
Normally made of cast iron
May be integral part of wheel hub
  In many front-wheel-drive vehicles, disc and hub are separate units
May be solid or ventilated

## Slide 45: Disc Brake Types
Floating caliper disc brake
  Mounted on two bolts supported by rubber bushings
  This one-piston caliper is free to shift, or float, in rubber bushings
Sliding caliper disc brake
  One-piston caliper that is mounted in slots machined in caliper adapter
  Caliper is free to slide sideways in slots or grooves as linings wear

## Slide 46: Disc Brake Types
Fixed caliper disc brake
  Uses more than one piston and caliper cylinder
  The caliper is bolted directly to the steering knuckle
    It is not free to move in relation to the disc
  Severe vibrations can occur with a slight runout of the disc

## Slide 47: Disc Brake Assembly
(Chrysler and Toyota)

## Slide 48: Drum Brake Assemblies
Drum brakes
  Have large drum that surrounds brake shoes and hydraulic wheel cylinder
Drum brake assembly consists of backing plate, wheel cylinder, brake shoes and linings, retracting springs, hold-down springs, brake drum, and automatic adjusting mechanism

## Slide 49: Drum Brake Assembly
(Chrysler and Toyota)

## Slide 50: Backing Plate
Brake backing plate
  Holds shoes, springs, wheel cylinder, and other parts inside brake drum
Helps keep road dirt and water off brakes
Backing plate bolts to axle housing or spindle support

## Slide 51: Wheel Cylinder Assembly
Wheel cylinder
  Consists of cylinder or housing, expander spring, rubber cups, pistons, dust boots, and bleeder screw
Wheel cylinder housing
  Forms enclosure for other parts of assembly
Wheel cylinder boots
  Keeps road dirt and water out of cylinder

## Slide 52: Wheel Cylinder Assembly (Cont.)
Wheel cylinder pistons
  Metal or plastic plungers transfer force out of wheel cylinder assembly
Wheel cylinder cups
  Rubber seals that keep fluid from leaking past pistons
Wheel cylinder spring
  Helps hold rubber cups against pistons when wheel cylinder assembly is not pressurized

## Slide 53: Wheel Cylinder Assembly (Cont.)
Cup expanders
  Press outer edges of cups against wall of wheel cylinder
Bleeder screw
  Provides means of removing air from brake system
  Threads into hole in back of wheel cylinder

## Slide 54: Drum Brake Shoes
Drum brake shoe assemblies or brake shoes
  Rub against revolving brake drum to produce braking action
Primary brake shoe
  Front shoe, it has slightly shorter lining than secondary shoe
Secondary brake shoe
  Rear shoe, it has largest lining surface area

## Slide 55: Retracting Springs and Hold-Down Springs
Retracting springs
  Pull brake shoes away from brake drums when brake pedal is released
Hold-down springs
  Hold brake shoes against backing plate when brakes are in released position

## Slide 56: Brake Shoe Adjusters
Brake shoe adjusters
  Maintain correct drum-to-lining clearance as brake linings wear
Many vehicles use star wheel-type brake shoe adjusting mechanism
  Adjusting screw assembly
Other vehicles use latch-type adjusters
Automatic brake shoe adjusters function when brakes are applied with vehicle moving in reverse

## Slide 57: Brake Drums
Provide rubbing surface for brake shoe linings
Fits over wheel lug studs
Large hole in middle of drum centers drum on front hub or rear axle flange
Wheel and drum turn as unit
(Ford)

## Slide 58: Brake Shoe Energization
When brake shoes are forced against rotating drum, they are pulled away from their pivot point by friction
This self-energizing action draws shoes tighter against drum
(EIS)

## Slide 59: Brake Shoe Energization (Cont.)
With most drum brake designs, shoe energization is supplemented by servo action
Servo action results when primary (front) shoe helps apply secondary (rear) shoe
(EIS)

## Slide 60: Brake System Switches
Three types of switches
Stoplight switch
Brake warning light switch
Low-fluid warning light switch

## Slide 61: Brake System Switches (Cont.)
Stoplight switch
  Spring-loaded electrical switch that operates rear brake lights of vehicle
Brake warning light switch or pressure differential valve
  Warns driver of pressure loss on one side of dual brake system
Low-fluid warning light switch
  Turns on dash light if brake fluid in master cylinder becomes low

## Slide 62: Brake System Control Valves
Metering valve
  Designed to equalize braking action at each wheel during light brake applications
Proportioning valve
  Used to equalize braking action in systems with front disc brakes and rear drum brakes
Combination valve
  Single unit that functions as brake warning light switch, metering valve, and/or proportioning valve

## Slide 63: Parking Brakes
Parking brakes or emergency brakes
  Provide mechanical means of applying brakes
    Cable and levers
Electric parking brake
  Uses brake system control module to operate electric servo motor that mechanically engages rear brakes

## Slide 64: Parking Brakes (Cont.)
(Toyota)

## Slide 65: Parking Brakes (Cont.)
(Chrysler and Ford)

## Slide 66: Hybrid Brakes
Today’s hybrid vehicles are equipped with regenerative braking systems
Electric braking systems
Work with conventional hydraulic brakes to slow vehicle and generate electricity to recharge vehicle’s HV battery at the same time