## Slide 2: 82
Anti-Lock Brakes, Traction Control, and Stability Control
Chapter

## Slide 3: Objectives
After studying this chapter, you will be able to:
Identify the major parts of a typical anti-lock brake system.
Describe the operation of anti-lock brake systems.
Compare anti-lock brake design variations.
Describe the purpose and operation of traction control and stability control systems.

## Slide 4: Objectives
Diagnose problems in anti-lock brake systems.
Repair anti-lock brake systems.
Diagnose and repair traction control and stability control systems.
Correctly answer ASE certification test questions requiring a knowledge of anti-lock brake systems, traction control systems, and stability control systems.

## Slide 5: Anti-Lock Brakes, Traction Control, and Stability Control−Introduction
Anti-lock brake systems or ABS
  Increase safety by reducing stopping distances compared to manual brakes on both wet and dry pavement
Traction control systems (TCS)
  Electronically controls brakes, differential, engine, and transaxle to help reduce tire spin upon acceleration on slippery pavement

## Slide 6: Anti-Lock Brakes, Traction Control, and Stability Control−Introduction (Cont.)
Stability control systems
  Electronically link steering, suspension, braking, and traction control systems together to prevent loss of vehicle control and skidding when cornering at high speed
This chapter will introduce additional parts needed to provide computer control of complete chassis and driveline

## Slide 7: Anti-Lock Brake Systems (ABS)
Uses wheel speed sensors, ABS control module, electro-hydraulic brake actuator, and conventional hydraulic brake circuits to prevent wheel lockup during hard braking
Improves driver and passenger safety by reducing stopping distances and increasing directional stability under panic stop conditions

## Slide 8: ABS Components
Major parts of anti-lock braking system
Wheel speed sensors
  Magnetic pickups for detecting rotating speed of each tire and wheel assembly
Sensor trigger wheels
  Toothed wheels that rotate at same rpms as wheel and tire
ABS control module
  Small computer, or processor, that uses sensor inputs to control electro-hydraulic modulator

## Slide 9: ABS Components (Cont.)
Electro-hydraulic modulator
  Cycles pressure to each wheel brake cylinder if speed begins to slow down too much, indicating tire skid or wheel lockup
Brake warning light
  Informs driver of problems in anti-lock brake system circuits

## Slide 10: ABS Components (Cont.)
(Honda)

## Slide 11: Wheel Speed Sensors
Produce ac signals that correspond to wheel and tire speed
  These signals feed into ABS control module
With rear-wheel anti-lock brakes, wheel speed sensors are only on rear wheels
With four-wheel antilock brakes, wheel speed sensors needed on all wheels

## Slide 12: Wheel Speed Sensors (Cont.)
Sensor rotor or trigger wheel
  Toothed ring that rotates with wheel hub
  Magnetic sensor tip located next to sensor rotor teeth
  Only small air gap separates sensor tip from spinning teeth
(Saab)

## Slide 13: Wheel Speed Sensors (Cont.)
Frequency of wheel speed sensors ac signal depends on tire and wheel speed
ABS control module uses ac signal to check for tire skid
Rapid decrease in sensor ac signal frequency would indicate that tire is starting to lock up and skid

## Slide 14: Wheel Speed Sensors (Cont.)

## Slide 15: ABS Control Module
Small computer that uses wheel speed sensor inputs to control operation of electro-hydraulic modulator
(Chrysler)

## Slide 16: ABS Electro-Hydraulic Modulator
ABS electro-hydraulic modulator or ABS actuator
  Regulates fluid pressure applied to each wheel brake assembly during periods of hard braking
ABS control module controls modulator

## Slide 17: ABS Electro-Hydraulic Modulator (Cont.)
Major parts of ABS modulator
Brake fluid reservoir
  Container for holding extra supply of brake fluid
Brake solenoid valve block
  Electro-hydraulic device with coil-operated valves that control brake fluid flow to each wheel brake cylinder

## Slide 18: ABS Electro-Hydraulic Modulator (Cont.)
Brake accumulator
  Chamber for storing extra fluid under high pressure
Brake fluid pump and motor
  High-pressure pump operated by small electric motor
  It provides brake fluid pressure for ABS system

## Slide 19: ABS Electro-Hydraulic Modulator (Cont.)
Brake pressure switch
  Sensor that monitors brake fluid pressure and controls operation of electric motor for hydraulic pump
Brake master cylinder-booster assembly
  Conventional master cylinder with power assist for operating brakes under normal conditions

## Slide 20: ABS Electro-Hydraulic Modulator (Cont.)
Integrated ABS
  Combines power booster, master cylinder, and modulator units into one assembly
Nonintegrated ABS
  Major units are separated
  Conventional booster and master cylinder are used with separate electro-hydraulic modulator

## Slide 21: ABS Electro-Hydraulic Modulator (Cont.)
Hydraulic pressure modulation
  Refers to electro-hydraulic unit’s ability to rapidly cycle pressure to wheel cylinders or calipers on and off, preventing wheel lockup and skidding

## Slide 22: ABS Electro-Hydraulic Modulator (Cont.)
Three modes of ABS pressure modulation
Isolation mode
  ABS control module detects that tire is starting to skid and energizes modulator to isolate that hydraulic circuit from other brake lines

## Slide 23: ABS Electro-Hydraulic Modulator (Cont.)
Dump mode
  ABS releases hydraulic pressure to one or more of brake wheel cylinders or calipers
  Done to stop tire skidding
Reapply mode
  ABS applies hydraulic pressure to one or more of wheel brake assemblies
  Done to reapply brakes during pressure modulation

## Slide 24: ABS Warning Light
Light mounted in dash used to alert driver to ABS malfunction
Light glows during engine cranking and stays on for several seconds after engine starts
Informs you that system is armed and functioning

## Slide 25: ABS Channels
Separate hydraulic circuit that feeds out to one or more wheel cylinders or caliper pistons
Anti-lock brake systems have from one to four channels
One-channel ABS
  Operates rear wheel brakes together
  Only one channel is provided for both rear wheels

## Slide 26: ABS Channels (Cont.)
Two-channel ABS
  Two separate hydraulic circuits controlled by electro-hydraulic modulator
  With rear-wheel ABS, each rear brake has its own hydraulic control circuit
Four-channel ABS
  Separate hydraulic control circuit for each wheel
  Most effective and common anti-lock brake system

## Slide 27: ABS Operation
Under normal braking conditions, ABS is not used
If brakes are applied in panic stop and wheel begins to lock up, ABS is activated
Wheel sensor on slowing wheel instantly reduces frequency of ac signal sent to ABS control module

## Slide 28: ABS Operation (Cont.)
Control module detects that wheel is slowing down more than others and is getting ready to slide or skid
Module then sends electrical current to correct solenoid on electro-hydraulic modulator assembly to bleed pressure from that channel

## Slide 29: Traction and Stability Control Systems
Most traction control systems work with antilock brake system to cycle hydraulic pressure to wheel spinning fastest
Control module is capable of applying one wheel brake at a time
Some systems also reduce engine power output to reduce skidding
Indicator light comes on when traction control system is activated

## Slide 30: Traction and Stability Control Systems (Cont.)
Designed to make vehicle more stable under emergency handling situations, such as when trying to avoid collision
If understeer is detected, control module applies braking force to rear inside wheel
If oversteer is detected, additional braking force is automatically applied to outside front wheel

## Slide 31: Traction and Stability Control Systems (Cont.)
Stability control system may use inputs from these sensors
Steering angle sensor
  Measures how sharply steering wheel is rotated to right or left
Lateral acceleration sensor
  Measures how much side force is generated by turn

## Slide 32: Traction and Stability Control Systems (Cont.)
Yaw sensor
  Measures direction of thrust generated by vehicle movement
Throttle position sensor
  Measures how far driver has pressed down on accelerator to control engine power output

## Slide 33: Traction and Stability Control Systems (Cont.)
Brake pressure sensor
  Measures amount of hydraulic pressure produced by driver pressing on brake pedal
Other sensors
  Give control module information about driver’s actions and resulting vehicle motion

## Slide 34: ABS Service
Before servicing an anti-lock brake system, be familiar with how an operating system works and feels
Since designs and repair procedures vary, read service manual for vehicle
This gives you information needed
  Diagnosis charts, part locations, specifications, procedures, etc.

## Slide 35: ABS Service (Cont.)
Check
ABS indicator light on
Low or contaminated brake fluid
Brake fluid leaks, especially at modulator seals, gaskets, and lines
Worn or damaged brake pad linings and rotors
Tires that will not rotate freely

## Slide 36: ABS Service (Cont.)
Loose or worn wheel bearings, which could affect wheel speed sensor operation
Badly worn tires or tires of unequal size, which could upset ABS operation
Damaged or improperly mounted speed sensors and trigger wheels

## Slide 37: Scanning ABS
Typical ABS diagnostic system can produce over 50 trouble codes to help find cause of malfunction
If ABS light stays on more than several seconds after vehicle is started, ABS control module has detected abnormal operating condition

## Slide 38: Scanning ABS (Cont.)
Use scan tool to check code history
  List of stored codes with number of times each has occurred
This will let you know how often problem occurs
Review all trouble codes
  May help you quickly find bad ABS component or circuit

## Slide 39: Scanning ABS (Cont.)
Scan tool will normally indicate problems with the following
  Wheel speed sensor circuits
  ABS warning light circuit
  System relays
  Low system voltage
  Modulator motors

## Slide 40: Scanning ABS (Cont.)
  Solenoid circuits
  Brake switch circuit
  Calibration memory in the ABS control module
  Other circuits and components
Scan tool can perform several manual and automatic tests and obtain system values

## Slide 41: ABS Pinpoint Tests
If scan tool indicates malfunction, still use pinpoint tests to determine exact problem source
Use multimeter to check circuit or component
Compare meter readings to factory specifications to verify trouble

## Slide 42: ABS Speed Sensor Service
If scan tool points to problem with wheel speed sensor
Make sure sensor is mounted securely
Check that all wire connectors are tight
Check for chipped or broken trigger wheel teeth
Check air gap between speed sensor and its trigger wheel

## Slide 43: ABS Speed Sensor Service (Cont.)
Handheld scope will check exact signal output from suspicious wheel speed sensor
Unplug wiring to sensor and connect scope to sensor’s output leads
To generate waveform, spin wheel by hand
Compare actual sensor waveform to known good waveform
If sensor is bad, replace it

## Slide 44: ABS Modulator Check
Place vehicle on jack stands so all four tires are equally off ground
Release parking brake
Rotate each wheel by hand
Make sure no wheels drag.
Connect jumper wire to correct terminals on vehicle’s diagnostic connector or use scan tool to energize modulator to apply hydraulic pressure to one of wheels

## Slide 45: ABS Modulator Check (Cont.)
Press down and hold brake pedal while you have a helper make sure that wheel will not rotate
Using service manual instructions, energize modulator to dump pressure to wheel
  Make sure modulator relieves pressure from wheel cylinder so tire will rotate freely

## Slide 46: ABS Modulator Service
If ABS modulator is faulty, most shops install new or factory-rebuilt unit
Modulators are very complex and time-consuming to rebuild
If vehicle is under warranty, some dealerships repair or rebuild modulators in-house

## Slide 47: ABS Modulator Service (Cont.)
General rules when repairing or replacing ABS modulator include
Always install all parts included in rebuild kit
If installing new unit, make sure part number is correct
Always lubricate rubber parts with clean brake fluid of appropriate type

## Slide 48: ABS Modulator Service (Cont.)
Work on clean, uncluttered workbench to avoid contamination
Avoid using compressed air on hydraulic parts
Oil from compressor may deteriorate rubber parts
Prevent brake fluid from contacting electrical connections, painted surfaces, and electronic parts

## Slide 49: ABS Modulator Service (Cont.)
Use correct torque values when tightening fasteners
Refer to service manual for detailed procedures, specifications, and safety precautions

## Slide 50: ABS Modulator Service (Cont.)

## Slide 51: Regenerative Braking Safety
Pull out HV battery disconnect
Disconnect 12-V battery negative cable
Pull off ABS control module connector
Remove related fuses or circuit breakers to keep all sources of power from reaching ABS control module

## Slide 52: Regenerative Braking Safety (Cont.)
If you accidentally reconnect battery power to ABS control circuit, it might perform automatic pressure test to check brake fluid leakage
During pressure test, ABS pump motor applies full hydraulic pressure to all four brake calipers
Your fingers could be crushed if hydraulic piston shoots from its bore at full brake line pressure!

## Slide 53: ABS Bleeding
When master cylinder is formed as integral part of modulator, use very specific bleeding procedure
Electrical breakout box and electronic unit might be required to properly energize solenoids when bleeding some systems

## Slide 54: ABS Wet Pavement Test
Wet pavement test is performed with two tires on wet pavement and other two tires on dry pavement
Position vehicle so that only right or left tires ride on wet area
Drive vehicle across strip of wet pavement at about five miles per hour
Hit brakes hard to try to make tires skid on pavement

## Slide 55: ABS Wet Pavement Test (Cont.)
Ask a helper to watch tire contact on wet pavement and let you know if either tire is totally locking up or not modulating upon hard brake application
As you brake and two of tires try to skid, you should feel pedal modulate
Helper should not see tires lock up or continue to rotate freely
ABS system should modulate hydraulic pressure so tires almost skid

## Slide 56: Traction and Stability Control System Service
Diagnosis and repair procedures for traction and stability control systems are similar to methods described for ABS
Use initial inspection and scan tool to find any obvious problems or trouble codes
If you have trouble codes, use pinpoint tests to verify problem

## Slide 57: Final System Check
Clear trouble codes and re-scan system for problems
Check brake fluid level in system
Test-drive vehicle in area without traffic
Simulate panic stop several times in large parking lot
Make sure ABS indicator light stays off